## Slide 1
Digital Design and Computer Architecture, 2nd Edition
Chapter 8
David Money Harris and Sarah L. Harris

## Slide 2
Chapter 8 :: Topics
Introduction
Memory System Performance Analysis
Caches
Virtual Memory
Memory-Mapped I/O
Summary

## Slide 3
Computer performance depends on:
  Processor performance
  Memory system performance
Memory Interface
Introduction

## Slide 4
In prior chapters, assumed access memory in 1 clock cycle – but hasn’t been true since the 1980’s
Processor-Memory Gap

## Slide 5
Make memory system appear as fast as processor
Use hierarchy of memories
Ideal memory:
  Fast
  Cheap (inexpensive)
  Large (capacity)
But can only choose two!
Memory System Challenge

## Slide 6
Memory Hierarchy

## Slide 7
Exploit locality to make memory accesses fast
Temporal Locality:
  Locality in time
  If data used recently, likely to use it again soon
  How to exploit: keep recently accessed data in higher levels of memory hierarchy
Spatial Locality:
  Locality in space
  If data used recently, likely to use nearby data soon
  How to exploit: when access data, bring nearby data into higher levels of memory hierarchy too
Locality

## Slide 8
Hit: data found in that level of memory hierarchy
Miss: data not found (must go to next level)
Hit Rate = # hits / # memory accesses
= 1 – Miss Rate
Miss Rate = # misses / # memory accesses
= 1 – Hit Rate
Average memory access time (AMAT): average time for processor to access data
AMAT = tcache + MRcache[tMM + MRMM(tVM)]
Memory Performance

## Slide 9
A program has 2,000 loads and stores
1,250 of these data values in cache
Rest supplied by other levels of memory hierarchy
What are the hit and miss rates for the cache?
Memory Performance Example 1

## Slide 10
A program has 2,000 loads and stores
1,250 of these data values in cache
Rest supplied by other levels of memory hierarchy
What are the hit and miss rates for the cache?
Hit Rate = 1250/2000 = 0.625
Miss Rate = 750/2000 = 0.375 = 1 – Hit Rate
Memory Performance Example 1

## Slide 11
Suppose processor has 2 levels of hierarchy: cache and main memory
tcache = 1 cycle, tMM = 100 cycles
What is the AMAT of the program from Example 1?
Memory Performance Example 2

## Slide 12
Suppose processor has 2 levels of hierarchy: cache and main memory
tcache = 1 cycle, tMM = 100 cycles
What is the AMAT of the program from Example 1?
AMAT = tcache + MRcache(tMM)
= [1 + 0.375(100)] cycles
= 38.5 cycles
Memory Performance Example 2

## Slide 13
Highest level in memory hierarchy
Fast (typically ~ 1 cycle access time)
Ideally supplies most data to processor
Usually holds most recently accessed data
Cache

## Slide 14
What data is held in the cache?
How is data found?
What data is replaced?
Focus on data loads, but stores follow same principles
Cache Design Questions

## Slide 15
Ideally, cache anticipates needed data and puts it in cache
But impossible to predict future
Use past to predict future – temporal and spatial locality:
  Temporal locality: copy newly accessed data into cache
  Spatial locality: copy neighboring data into cache too
What data is held in the cache?

## Slide 16
Capacity (C):
  number of data bytes in cache
Block size (b):
  bytes of data brought into cache at once
Number of blocks (B = C/b):
  number of blocks in cache: B = C/b
Degree of associativity (N):
  number of blocks in a set
Number of sets (S = B/N):
  each memory address maps to exactly one cache set
Cache Terminology

## Slide 17
Cache organized into S sets
Each memory address maps to exactly one set
Caches categorized by # of blocks in a set:
  Direct mapped: 1 block per set
  N-way set associative: N blocks per set
  Fully associative: all cache blocks in 1 set
Examine each organization for a cache with:
  Capacity (C = 8 words)
  Block size (b = 1 word)
  So, number of blocks (B = 8)
How is data found?

## Slide 18
C = 8 words (capacity)
b = 1 word (block size)
So, B = 8 (# of blocks)
Ridiculously small, but will illustrate organizations
Example Cache Parameters

## Slide 19
Direct Mapped Cache

## Slide 20
Direct Mapped Cache Hardware

## Slide 21
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = ?
Direct Mapped Cache Performance

## Slide 22
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 3/15
= 20%
Temporal Locality
Compulsory Misses
Direct Mapped Cache Performance

## Slide 23
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = ?
Direct Mapped Cache: Conflict

## Slide 24
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 10/10
= 100%
Conflict Misses
Direct Mapped Cache: Conflict

## Slide 25
N-Way Set Associative Cache

## Slide 26
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = ?
N-Way Set Associative Performance

## Slide 27
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 2/10
= 20%
Associativity reduces
conflict misses
N-Way Set Associative Performance

## Slide 28
Reduces conflict misses
Expensive to build
Fully Associative Cache

## Slide 29
Increase block size:
  Block size, b = 4 words
  C = 8 words
  Direct mapped (1 block per set)
  Number of blocks, B = 2 (C/b = 8/4 = 2)
Spatial Locality?

## Slide 30
Cache with Larger Block Size

## Slide 31
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = ?
Direct Mapped Cache Performance

## Slide 32
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 1/15
= 6.67%
Larger blocks
reduce compulsory misses
through spatial locality
Direct Mapped Cache Performance

## Slide 33
Capacity: C
Block size: b
Number of blocks in cache: B = C/b
Number of blocks in a set: N
Number of sets: S = B/N
Organization | Number of Ways (N) | Number of Sets (S = B/N)
Direct Mapped | 1 | B
N-Way Set Associative | 1 < N < B | B / N
Fully Associative | B | 1
Cache Organization Recap

## Slide 34
Cache is too small to hold all data of interest at once
If cache full: program accesses data X & evicts data Y
Capacity miss when access Y again
How to choose Y to minimize chance of needing it again?
Least recently used (LRU) replacement: the least recently used block in a set evicted
Capacity Misses

## Slide 35
Compulsory: first time data accessed
Capacity: cache too small to hold all data of interest
Conflict: data of interest maps to same location in cache
Miss penalty: time it takes to retrieve a block from lower level of hierarchy
Types of Misses

## Slide 36
# MIPS assembly
lw $t0, 0x04($0)
lw $t1, 0x24($0)
lw $t2, 0x54($0)
LRU Replacement

## Slide 37
# MIPS assembly
lw $t0, 0x04($0)
lw $t1, 0x24($0)
lw $t2, 0x54($0)
LRU Replacement

## Slide 38
What data is held in the cache?
  Recently used data (temporal locality)
  Nearby data (spatial locality)
How is data found?
  Set is determined by address of data
  Word within block also determined by address
  In associative caches, data could be in one of several ways
What data is replaced?
  Least-recently used way in the set
Cache Summary

## Slide 39
Bigger caches reduce capacity misses
Greater associativity reduces conflict misses
Adapted from Patterson & Hennessy, Computer Architecture: A Quantitative Approach, 2011
Miss Rate Trends

## Slide 40
Bigger blocks reduce compulsory misses
Bigger blocks increase conflict misses
Miss Rate Trends

## Slide 41
Larger caches have lower miss rates, longer access times
Expand memory hierarchy to multiple levels of caches
Level 1: small and fast (e.g. 16 KB, 1 cycle)
Level 2: larger and slower (e.g. 256 KB, 2-6 cycles)
Most modern PCs have L1, L2, and L3 cache
Multilevel Caches

## Slide 42
Intel Pentium III Die

## Slide 43
Gives the illusion of bigger memory
Main memory (DRAM) acts as cache for hard disk
Virtual Memory

## Slide 44
Physical Memory: DRAM (Main Memory)
Virtual Memory: Hard drive
  Slow, Large, Cheap
Memory Hierarchy

## Slide 45
Takes milliseconds to seek correct location on disk
Hard Disk

## Slide 46
Virtual addresses
  Programs use virtual addresses
  Entire virtual address space stored on a hard drive
  Subset of virtual address data in DRAM
  CPU translates virtual addresses into physical addresses (DRAM addresses)
  Data not in DRAM fetched from hard drive
Memory Protection
  Each program has own virtual to physical mapping
  Two programs can use same virtual address for different data
  Programs don’t need to be aware others are running
  One program (or virus) can’t corrupt memory used by another
Virtual Memory

## Slide 47
Cache | Virtual Memory
Block | Page
Block Size | Page Size
Block Offset | Page Offset
Miss | Page Fault
Tag | Virtual Page Number
Physical memory acts as cache for virtual memory
Cache/Virtual Memory Analogues

## Slide 48
Page size: amount of memory transferred from hard disk to DRAM at once
Address translation: determining physical address from virtual address
Page table: lookup table used to translate virtual addresses to physical addresses
Virtual Memory Definitions

## Slide 49
Most accesses hit in physical memory
But programs have the large capacity of virtual memory
Virtual & Physical Addresses

## Slide 50
Address Translation

## Slide 51
System:
  Virtual memory size: 2 GB = 231 bytes
  Physical memory size: 128 MB = 227 bytes
  Page size: 4 KB = 212 bytes
Virtual Memory Example

## Slide 52
System:
  Virtual memory size: 2 GB = 231 bytes
  Physical memory size: 128 MB = 227 bytes
  Page size: 4 KB = 212 bytes
Organization:
  Virtual address: 31 bits
  Physical address: 27 bits
  Page offset: 12 bits
  # Virtual pages = 231/212 = 219 (VPN = 19 bits)
  # Physical pages = 227/212 = 215 (PPN = 15 bits)
Virtual Memory Example

## Slide 53
19-bit virtual page numbers
15-bit physical page numbers
Virtual Memory Example

## Slide 54
Virtual Memory Example
What is the physical address of virtual address 0x247C?

## Slide 55
Virtual Memory Example
What is the physical address of virtual address 0x247C?
  VPN = 0x2
  VPN 0x2 maps to PPN 0x7FFF
  12-bit page offset: 0x47C
  Physical address = 0x7FFF47C

## Slide 56
Page table
  Entry for each virtual page
  Entry fields:
    Valid bit: 1 if page in physical memory
    Physical page number: where the page is located
How to perform translation?

## Slide 57
VPN is index into page table
Page Table Example

## Slide 58
What is the physical address of virtual address 0x5F20?
Page Table Example 1

## Slide 59
What is the physical address of virtual address 0x5F20?
  VPN = 5
  Entry 5 in page table VPN 5 => physical page 1
  Physical address: 0x1F20
Page Table Example 1

## Slide 60
What is the physical address of virtual address 0x73E0?
Page Table Example 2

## Slide 61
What is the physical address of virtual address 0x73E0?
  VPN = 7
  Entry 7 is invalid
  Virtual page must be paged into physical memory from disk
Page Table Example 2

## Slide 62
Page table is large
  usually located in physical memory
Load/store requires 2 main memory accesses:
  one for translation (page table read)
  one to access data (after translation)
Cuts memory performance in half
  Unless we get clever…
Page Table Challenges

## Slide 63
Small cache of most recent translations
Reduces # of memory accesses for most loads/stores from 2 to 1
Translation Lookaside Buffer (TLB)

## Slide 64
Page table accesses: high temporal locality
  Large page size, so consecutive loads/stores likely to access same page
TLB
  Small: accessed in < 1 cycle
  Typically 16 - 512 entries
  Fully associative
  > 99 % hit rates typical
  Reduces # of memory accesses for most loads/stores from 2 to 1
TLB

## Slide 65
Example 2-Entry TLB

## Slide 66
Multiple processes (programs) run at once
Each process has its own page table
Each process can use entire virtual address space
A process can only access physical pages mapped in its own page table
Memory Protection

## Slide 67
Virtual memory increases capacity
A subset of virtual pages in physical memory
Page table maps virtual pages to physical pages – address translation
A TLB speeds up address translation
Different page tables for different programs provides memory protection
Virtual Memory Summary

## Slide 68
Processor accesses I/O devices just like memory (like keyboards, monitors, printers)
Each I/O device assigned one or more address
When that address is detected, data read/written to I/O device instead of memory
A portion of the address space dedicated to I/O devices
Memory-Mapped I/O

## Slide 69
Address Decoder:
  Looks at address to determine which device/memory communicates with the processor
I/O Registers:
  Hold values written to the I/O devices
ReadData Multiplexer:
  Selects between memory and I/O devices as source of data sent to the processor
Memory-Mapped I/O Hardware

## Slide 70
The Memory Interface

## Slide 71
Memory-Mapped I/O Hardware

## Slide 72
Suppose I/O Device 1 is assigned the address 0xFFFFFFF4
  Write the value 42 to I/O Device 1
  Read value from I/O Device 1 and place in $t3
Memory-Mapped I/O Code

## Slide 73
Write the value 42 to I/O Device 1 (0xFFFFFFF4)
  addi $t0, $0, 42
  sw $t0, 0xFFF4($0)
Memory-Mapped I/O Code

## Slide 74
Read the value from I/O Device 1 and place in $t3
  lw $t3, 0xFFF4($0)
Memory-Mapped I/O Code