## Slide 1
Digital Design and Computer Architecture, 2nd Edition
Chapter 7
David Money Harris and Sarah L. Harris

## Slide 2
Chapter 7 :: Topics
Introduction
Performance Analysis
Single-Cycle Processor
Pipelined Processor

## Slide 3
Microarchitecture: how to implement an architecture in hardware
Processor:
  Datapath: functional blocks
  Control: control signals
Introduction

## Slide 4
Multiple implementations for a single architecture:
  Single-cycle: Each instruction executes in a single cycle
  Multicycle: Each instruction is broken into series of shorter steps
  Pipelined: Each instruction broken up into series of steps & multiple instructions execute at once
Microarchitecture

## Slide 5
Program execution time
Execution Time = (#instructions)(cycles/instruction)(seconds/cycle)
Definitions:
  CPI: Cycles/instruction
  clock period: seconds/cycle
  IPC: instructions/cycle = IPC
Challenge is to satisfy constraints of:
  Cost
  Power
  Performance
Processor Performance

## Slide 6
Consider subset of MIPS instructions:
  R-type instructions: and, or, add, sub, slt
  Memory instructions: lw, sw
  Branch instructions: beq
MIPS Processor

## Slide 7
Determines everything about a processor:
  PC
  32 registers
  Memory
Architectural State

## Slide 8
MIPS State Elements

## Slide 9
Datapath
Control
Single-Cycle MIPS Processor

## Slide 10
STEP 1: Fetch instruction
Single-Cycle Datapath: lw fetch

## Slide 11
STEP 2: Read source operands from RF
Single-Cycle Datapath: lw Register Read

## Slide 12
STEP 3: Sign-extend the immediate
Single-Cycle Datapath: lw Immediate

## Slide 13
STEP 4: Compute the memory address
Single-Cycle Datapath: lw address

## Slide 14
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT
Review: ALU

## Slide 15
STEP 5: Read data from memory and write it back to register file
Single-Cycle Datapath: lw Memory Read

## Slide 16
STEP 6: Determine address of next instruction
Single-Cycle Datapath: lw PC Increment

## Slide 17
Write data in rt to memory
Single-Cycle Datapath: sw

## Slide 18
Read from rs and rt
Write ALUResult to register file
Write to rd (instead of rt)
Single-Cycle Datapath: R-Type

## Slide 19
Determine whether values in rs and rt are equal
Calculate branch target address:
BTA = (sign-extended immediate << 2) + (PC+4)
Single-Cycle Datapath: beq

## Slide 20
Single-Cycle Processor

## Slide 21
Single-Cycle Control

## Slide 22
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT
Review: ALU

## Slide 23
Review: ALU

## Slide 24
ALUOp1:0 | Meaning
00 | Add
01 | Subtract
10 | Look at Funct
11 | Not Used
ALUOp1:0 | Funct | ALUControl2:0
00 | X | 010 (Add)
01 | X | 110 (Subtract)
10 | 100000 (add) | 010 (Add)
10 | 100010 (sub) | 110 (Subtract)
10 | 100100 (and) | 000 (And)
10 | 100101 (or) | 001 (Or)
10 | 101010 (slt) | 111 (SLT)
Control Unit: ALU Decoder

## Slide 25
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 |  |  |  |  |  |  | 
lw | 100011 |  |  |  |  |  |  | 
sw | 101011 |  |  |  |  |  |  | 
beq | 000100 |  |  |  |  |  |  | 
Control Unit Main Decoder

## Slide 26
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 0 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
Control Unit: Main Decoder

## Slide 27
Single-Cycle Datapath: or

## Slide 28
No change to datapath
Extended Functionality: addi

## Slide 29
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
addi | 001000 |  |  |  |  |  |  | 
Control Unit: addi

## Slide 30
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
addi | 001000 | 1 | 0 | 1 | 0 | 0 | 0 | 00
Control Unit: addi

## Slide 31
Extended Functionality: j

## Slide 32
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0 | Jump
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10 | 0
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00 | 0
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00 | 0
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01 | 0
j | 000100 |  |  |  |  |  |  |  | 
Control Unit: Main Decoder

## Slide 33
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0 | Jump
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10 | 0
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00 | 0
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00 | 0
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01 | 0
j | 000100 | 0 | X | X | X | 0 | X | XX | 1
Control Unit: Main Decoder

## Slide 34
Program Execution Time
= (#instructions)(cycles/instruction)(seconds/cycle)
= # instructions x CPI x TC
Review: Processor Performance

## Slide 35
TC limited by critical path (lw)
Single-Cycle Performance

## Slide 36
Single-cycle critical path:
Tc = tpcq_PC + tmem + max(tRFread, tsext + tmux) + tALU + tmem + tmux + tRFsetup
Typically, limiting paths are:
  memory, ALU, register file
  Tc = tpcq_PC + 2tmem + tRFread + tmux + tALU + tRFsetup
Single-Cycle Performance

## Slide 37
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 30
Register setup | tsetup | 20
Multiplexer | tmux | 25
ALU | tALU | 200
Memory read | tmem | 250
Register file read | tRFread | 150
Register file setup | tRFsetup | 20
Tc = ?
Single-Cycle Performance Example

## Slide 38
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 30
Register setup | tsetup | 20
Multiplexer | tmux | 25
ALU | tALU | 200
Memory read | tmem | 250
Register file read | tRFread | 150
Register file setup | tRFsetup | 20
Tc = tpcq_PC + 2tmem + tRFread + tmux + tALU + tRFsetup
= [30 + 2(250) + 150 + 25 + 200 + 20] ps
= 925 ps
Single-Cycle Performance Example

## Slide 39
Program with 100 billion instructions:
Execution Time = # instructions x CPI x TC
= (100 × 109)(1)(925 × 10-12 s)
= 92.5 seconds
Single-Cycle Performance Example

## Slide 40
Single-cycle:
  + simple
  cycle time limited by longest instruction (lw)
  2 adders/ALUs & 2 memories
Multicycle:
  + higher clock speed
  + simpler instructions run faster
  + reuse expensive hardware on multiple cycles
  - sequencing overhead paid many times
Same design steps: datapath & control
Multicycle MIPS Processor

## Slide 41
Temporal parallelism
Divide single-cycle processor into 5 stages:
  Fetch
  Decode
  Execute
  Memory
  Writeback
Add pipeline registers between stages
Pipelined MIPS Processor

## Slide 42
Single-Cycle vs. Pipelined

## Slide 43
Pipelined Processor Abstraction

## Slide 44
Single-Cycle & Pipelined Datapath

## Slide 45
WriteReg must arrive at same time as Result
Corrected Pipelined Datapath

## Slide 46
Same control unit as single-cycle processor
Control delayed to proper pipeline stage
Pipelined Processor Control

## Slide 47
When an instruction depends on result from instruction that hasn’t completed
Types:
  Data hazard: register value not yet written back to register file
  Control hazard: next instruction not decided yet (caused by branches)
Pipeline Hazards

## Slide 48
Data Hazard

## Slide 49
Insert nops in code at compile time
Rearrange code at compile time
Forward data at run time
Stall the processor at run time
Handling Data Hazards

## Slide 50
Insert enough nops for result to be ready
Or move independent useful instructions forward
Compile-Time Hazard Elimination

## Slide 51
Data Forwarding

## Slide 52
Data Forwarding

## Slide 53
Forward to Execute stage from either:
  Memory stage or
  Writeback stage
Forwarding logic for ForwardAE:
if ((rsE != 0) AND (rsE == WriteRegM) AND RegWriteM)
then ForwardAE = 10
else if ((rsE != 0) AND (rsE == WriteRegW) AND RegWriteW)
then ForwardAE = 01
else ForwardAE = 00
Forwarding logic for ForwardBE same, but replace rsE with rtE
Data Forwarding

## Slide 54
Stalling

## Slide 55
Stalling

## Slide 56
Stalling Hardware

## Slide 57
lwstall =
((rsD==rtE) OR (rtD==rtE)) AND MemtoRegE
StallF = StallD = FlushE = lwstall
Stalling Logic

## Slide 58
beq:
  branch not determined until 4th stage of pipeline
  Instructions after branch fetched before branch occurs
  These instructions must be flushed if branch happens
Branch misprediction penalty
  number of instruction flushed when branch is taken
  May be reduced by determining branch earlier
Control Hazards

## Slide 59
Control Hazards: Original Pipeline

## Slide 60
Control Hazards

## Slide 61
Introduced another data hazard in Decode stage
Early Branch Resolution

## Slide 62
Early Branch Resolution

## Slide 63
Handling Data & Control Hazards

## Slide 64
Forwarding logic:
ForwardAD = (rsD !=0) AND (rsD == WriteRegM) AND RegWriteM
ForwardBD = (rtD !=0) AND (rtD == WriteRegM) AND RegWriteM
Stalling logic:
branchstall = BranchD AND RegWriteE AND
(WriteRegE == rsD OR WriteRegE == rtD)
OR
BranchD AND MemtoRegM AND
(WriteRegM == rsD OR WriteRegM == rtD)
StallF = StallD = FlushE = lwstall OR branchstall
Control Forwarding & Stalling Logic

## Slide 65
Guess whether branch will be taken
  Backward branches are usually taken (loops)
  Consider history to improve guess
Good prediction reduces fraction of branches requiring a flush
Branch Prediction

## Slide 66
SPECINT2000 benchmark:
  25% loads
  10% stores
  11% branches
  2% jumps
  52% R-type
Suppose:
  40% of loads used by next instruction
  25% of branches mispredicted
  All jumps flush next instruction
What is the average CPI?
Pipelined Performance Example

## Slide 67
SPECINT2000 benchmark:
  25% loads
  10% stores
  11% branches
  2% jumps
  52% R-type
Suppose:
  40% of loads used by next instruction
  25% of branches mispredicted
  All jumps flush next instruction
What is the average CPI?
  Load/Branch CPI = 1 when no stalling, 2 when stalling
  CPIlw = 1(0.6) + 2(0.4) = 1.4
  CPIbeq = 1(0.75) + 2(0.25) = 1.25
  Average CPI = (0.25)(1.4) + (0.1)(1) + (0.11)(1.25) + (0.02)(2) + (0.52)(1)
  = 1.15
Pipelined Performance Example

## Slide 68
Pipelined processor critical path:
Tc = max {
tpcq + tmem + tsetup
2(tRFread + tmux + teq + tAND + tmux + tsetup )
tpcq + tmux + tmux + tALU + tsetup
tpcq + tmemwrite + tsetup
2(tpcq + tmux + tRFwrite) }
Pipelined Performance

## Slide 69
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 30
Register setup | tsetup | 20
Multiplexer | tmux | 25
ALU | tALU | 200
Memory read | tmem | 250
Register file read | tRFread | 150
Register file setup | tRFsetup | 20
Equality comparator | teq | 40
AND gate | tAND | 15
Memory write | Tmemwrite | 220
Register file write | tRFwrite | 100 ps
Tc = 2(tRFread + tmux + teq + tAND + tmux + tsetup )
= 2[150 + 25 + 40 + 15 + 25 + 20] ps = 550 ps
Pipelined Performance Example

## Slide 70
Program with 100 billion instructions
Execution Time = (# instructions) × CPI × Tc
= (100 × 109)(1.15)(550 × 10-12)
= 63 seconds
Pipelined Performance Example

## Slide 71
Processor | Execution Time (seconds) | Speedup (single-cycle as baseline)
Single-cycle | 92.5 | 1
Pipelined | 63 | 1.47
Processor Performance Comparison