## Slide 1: Machine-Level Programming II: Arithmetic & Control
Carnegie Mellon
Carnegie Mellon

## Slide 2: Today
Carnegie Mellon
Complete addressing mode, address computation (leal)
Arithmetic operations
Control: Condition codes
Conditional branches
While loops

## Slide 3: Complete Memory Addressing Modes
Carnegie Mellon
Most General Form
D(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]+ D]
  D: Constant “displacement” 1, 2, or 4 bytes
  Rb: Base register: Any of 8 integer registers
  Ri: Index register: Any, except for %esp
    Unlikely you’d use %ebp, either
  S: Scale: 1, 2, 4, or 8 (why these numbers?)
Special Cases
(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]]
D(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]+D]
(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]]

## Slide 4: Address Computation Instruction
Carnegie Mellon
leal Src,Dest
  Src is address mode expression
  Set Dest to address denoted by expression
Uses
  Computing addresses without a memory reference
    E.g., translation of p = &x[i];
  Computing arithmetic expressions of the form x + k*y
    k = 1, 2, 4, or 8
Example
int mul12(int x)
{
return x*12;
}
leal (%eax,%eax,2), %eax ;t <- x+x*2
sall $2, %eax ;return t<<2
Converted to ASM by compiler:

## Slide 5: Today
Carnegie Mellon
Complete addressing mode, address computation (leal)
Arithmetic operations
Control: Condition codes
Conditional branches
While loops

## Slide 6: Some Arithmetic Operations
Carnegie Mellon
Two Operand Instructions:
  Format Computation
    addl Src,Dest Dest = Dest + Src
    subl Src,Dest Dest = Dest  Src
    imull Src,Dest Dest = Dest * Src
    sall Src,Dest Dest = Dest << Src Also called shll
    sarl Src,Dest Dest = Dest >> Src Arithmetic
    shrl Src,Dest Dest = Dest >> Src Logical
    xorl Src,Dest Dest = Dest ^ Src
    andl Src,Dest Dest = Dest & Src
    orl Src,Dest Dest = Dest | Src
Watch out for argument order!
No distinction between signed and unsigned int (why?)

## Slide 7: Some Arithmetic Operations
Carnegie Mellon
One Operand Instructions
    incl Dest Dest = Dest + 1
    decl Dest Dest = Dest  1
    negl Dest Dest =  Dest
    notl Dest Dest = ~Dest
See book for more instructions

## Slide 8: Arithmetic Expression Example
Carnegie Mellon
int arith(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x+4;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 * t5;
return rval;
}
arith:
pushl %ebp
movl %esp, %ebp
movl 8(%ebp), %ecx
movl 12(%ebp), %edx
leal (%edx,%edx,2), %eax
sall $4, %eax
leal 4(%ecx,%eax), %eax
addl %ecx, %edx
addl 16(%ebp), %edx
imull %edx, %eax
popl %ebp
ret
Body
Set
Up
Finish

## Slide 9: Today
Carnegie Mellon
Complete addressing mode, address computation (leal)
Arithmetic operations
Control: Condition codes
Conditional branches
Loops

## Slide 10: Processor State (IA32, Partial)
Carnegie Mellon
Information about currently executing program
  Temporary data ( %eax, … )
  Location of runtime stack ( %ebp,%esp )
  Location of current code control point ( %eip, … )
  Status of recent tests ( CF, ZF, SF, OF )
%eip
General purpose
registers
Current stack top
Current stack frame
Instruction pointer
CF
ZF
SF
OF
Condition codes
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp

## Slide 11: Condition Codes (Implicit Setting)
Carnegie Mellon
Single bit registers
  CF Carry Flag (for unsigned) SF Sign Flag (for signed)
  ZF Zero Flag OF Overflow Flag (for signed)
Implicitly set (think of it as side effect) by arithmetic operations
  Example: addl/addq Src,Dest ↔ t = a+b
  CF set if carry out from most significant bit (unsigned overflow)
  ZF set if t == 0
  SF set if t < 0 (as signed)
  OF set if two’s-complement (signed) overflow (a>0 && b>0 && t<0) || (a<0 && b<0 && t>=0)
Not set by lea instruction
Full documentation (IA32), link on course website

## Slide 12: Condition Codes (Explicit Setting: Compare)
Carnegie Mellon
Explicit Setting by Compare Instruction
  cmpl/cmpq Src2, Src1
  cmpl b,a like computing a-b without setting destination
  CF set if carry out from most significant bit (used for unsigned comparisons)
  ZF set if a == b
  SF set if (a-b) < 0 (as signed)
  OF set if two’s-complement (signed) overflow (a>0 && b<0 && (a-b)<0) || (a<0 && b>0 && (a-b)>0)

## Slide 13: Condition Codes (Explicit Setting: Test)
Carnegie Mellon
Explicit Setting by Test instruction
  testl/testq Src2, Src1 testl b,a like computing a&b without setting destination
  Sets condition codes based on value of Src1 & Src2
  Useful to have one of the operands be a mask
  ZF set when a&b == 0
  SF set when a&b < 0

## Slide 14: Reading Condition Codes
Carnegie Mellon
SetX Instructions
  Set single byte based on combinations of condition codes
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF^OF)&~ZF | Greater (Signed)
setge | ~(SF^OF) | Greater or Equal (Signed)
setl | (SF^OF) | Less (Signed)
setle | (SF^OF)¦ZF | Less or Equal (Signed)
seta | ~CF&~ZF | Above (unsigned)
setb | CF | Below (unsigned)

## Slide 15: Reading Condition Codes (Cont.)
movl 12(%ebp),%eax # eax = y
cmpl %eax,8(%ebp) # Compare x : y
setg %al # al = x > y
movzbl %al,%eax # Zero rest of %eax
Carnegie Mellon
SetX Instructions:
  Set single byte based on combination of condition codes
One of 8 addressable byte registers
  Does not alter remaining 3 bytes
  Typically use movzbl to finish job
int gt (int x, int y)
{
return x > y;
}
Body
%eax | %ah | %al
%ecx | %ch | %cl
%edx | %dh | %dl
%ebx | %bh | %bl
%esi |  | 
%edi |  | 
%esp |  | 
%ebp |  | 

## Slide 16: Reading Condition Codes: x86-64
Carnegie Mellon
int gt (long x, long y)
{
return x > y;
}
cmpl %esi, %edi
setg %al
movzbl %al, %eax
Bodies
long lgt (long x, long y)
{
return x > y;
}
SetX Instructions:
  Set single byte based on combination of condition codes
  Does not alter remaining 3 bytes
Is %rax zero?
Yes: 32-bit instructions set high order 32 bits to 0!
cmpq %rsi, %rdi
setg %al
movzbl %al, %eax

## Slide 17: Today
Carnegie Mellon
Complete addressing mode, address computation (leal)
Arithmetic operations
x86-64
Control: Condition codes
Conditional branches & Moves
Loops

## Slide 18: Jumping
Carnegie Mellon
jX Instructions
  Jump to different part of code depending on condition codes
jX | Condition | Description
jmp | 1 | Unconditional
je | ZF | Equal / Zero
jne | ~ZF | Not Equal / Not Zero
js | SF | Negative
jns | ~SF | Nonnegative
jg | ~(SF^OF)&~ZF | Greater (Signed)
jge | ~(SF^OF) | Greater or Equal (Signed)
jl | (SF^OF) | Less (Signed)
jle | (SF^OF)¦ZF | Less or Equal (Signed)
ja | ~CF&~ZF | Above (unsigned)
jb | CF | Below (unsigned)

## Slide 19: Conditional Branch Example
Carnegie Mellon
int absdiff(int x, int y)
{
int result;
if (x > y) {
result = x-y;
} else {
result = y-x;
}
return result;
}
absdiff:
pushl %ebp
movl %esp, %ebp
movl 8(%ebp), %edx
movl 12(%ebp), %eax
cmpl %eax, %edx
jle .L6
subl %eax, %edx
movl %edx, %eax
jmp .L7
.L6:
subl %edx, %eax
.L7:
popl %ebp
ret
Body1
Setup
Finish
Body2b
Body2a

## Slide 20: Conditional Branch Example (Cont.)
Carnegie Mellon
int goto_ad(int x, int y)
{
int result;
if (x <= y) goto Else;
result = x-y;
goto Exit;
Else:
result = y-x;
Exit:
return result;
}
C allows “goto” as means of transferring control
  Closer to machine-level programming style
Generally considered bad coding style
absdiff:
pushl %ebp
movl %esp, %ebp
movl 8(%ebp), %edx
movl 12(%ebp), %eax
cmpl %eax, %edx
jle .L6
subl %eax, %edx
movl %edx, %eax
jmp .L7
.L6:
subl %edx, %eax
.L7:
popl %ebp
ret
Body1
Setup
Finish
Body2b
Body2a

## Slide 21: Using Conditional Moves
Carnegie Mellon
C Code
val = Test
? Then_Expr
: Else_Expr;
Goto Version
tval = Then_Expr;
result = Else_Expr;
t = Test;
if (t) result = tval;
return result;
Conditional Move Instructions
  Instruction supports:
    if (Test) Dest  Src
  Supported in post-1995 x86 processors
  GCC does not always use them
    Wants to preserve compatibility with ancient processors
    Enabled for x86-64
    Use switch –march=686 for IA32
Why?
  Branches are very disruptive to instruction flow through pipelines
  Conditional move do not require control transfer

## Slide 22: Conditional Move Example: x86-64
Carnegie Mellon
int absdiff(int x, int y) {
int result;
if (x > y) {
result = x-y;
} else {
result = y-x;
}
return result;
}
absdiff:
movl %edi, %edx
subl %esi, %edx # tval = x-y
movl %esi, %eax
subl %edi, %eax # result = y-x
cmpl %esi, %edi # Compare x:y
cmovg %edx, %eax # If >, result = tval
ret
x in %edi
y in %esi

## Slide 23: Today
Carnegie Mellon
Complete addressing mode, address computation (leal)
Arithmetic operations
x86-64
Control: Condition codes
Conditional branches and moves
Loops

## Slide 24: “Do-While” Loop Example
Carnegie Mellon
C Code
int pcount_do(unsigned x) {
int result = 0;
do {
result += x & 0x1;
x >>= 1;
} while (x);
return result;
}
Goto Version
int pcount_do(unsigned x)
{
int result = 0;
loop:
result += x & 0x1;
x >>= 1;
if (x)
goto loop;
return result;
}
Count number of 1’s in argument x (“popcount”)
Use conditional branch to either continue looping or to exit loop

## Slide 25: “Do-While” Loop Compilation
Carnegie Mellon
Goto Version
Registers:
  %edx x
  %ecx result
movl $0, %ecx # result = 0
.L2: # loop:
movl %edx, %eax
andl $1, %eax # t = x & 1
addl %eax, %ecx # result += t
shrl %edx # x >>= 1
jne .L2 # If !0, goto loop
int pcount_do(unsigned x) {
int result = 0;
loop:
result += x & 0x1;
x >>= 1;
if (x)
goto loop;
return result;
}

## Slide 26: General “Do-While” Translation
Carnegie Mellon
C Code
do
Body
while (Test);
Goto Version
loop:
Body
if (Test)
goto loop
Body:
Test returns integer
  = 0 interpreted as false
  ≠ 0 interpreted as true
{
Statement1;
Statement2;
…
Statementn;
}

## Slide 27: “While” Loop Example
Carnegie Mellon
C Code
Goto Version
Is this code equivalent to the do-while version?
  Must jump out of loop if test fails
int pcount_while(unsigned x) {
int result = 0;
while (x) {
result += x & 0x1;
x >>= 1;
}
return result;
}
int pcount_do(unsigned x) {
int result = 0;
if (!x) goto done;
loop:
result += x & 0x1;
x >>= 1;
if (x)
goto loop;
done:
return result;
}

## Slide 28: General “While” Translation
Carnegie Mellon
While version
while (Test)
Body
Do-While Version
if (!Test)
goto done;
do
Body
while(Test);
done:
Goto Version
if (!Test)
goto done;
loop:
Body
if (Test)
goto loop;
done:

## Slide 29: “For” Loop Example
Carnegie Mellon
C Code
Is this code equivalent to other versions?
#define WSIZE 8*sizeof(int)
int pcount_for(unsigned x) {
int i;
int result = 0;
for (i = 0; i < WSIZE; i++) {
unsigned mask = 1 << i;
result += (x & mask) != 0;
}
return result;
}

## Slide 30: “For” Loop Form
Carnegie Mellon
for (Init; Test; Update )
Body
General Form
for (i = 0; i < WSIZE; i++) {
unsigned mask = 1 << i;
result += (x & mask) != 0;
}
i = 0
i < WSIZE
i++
{
unsigned mask = 1 << i;
result += (x & mask) != 0;
}
Init
Test
Update
Body

## Slide 31: “For” Loop  While Loop
Carnegie Mellon
for (Init; Test; Update )
Body
For Version
Init;
while (Test ) {
Body
Update;
}
While Version

## Slide 32: “For” Loop  …  Goto
Carnegie Mellon
for (Init; Test; Update )
Body
For Version
Init;
while (Test ) {
Body
Update;
}
While Version
Init;
if (!Test)
goto done;
do
Body
Update
while(Test);
done:
Init;
if (!Test)
goto done;
loop:
Body
Update
if (Test)
goto loop;
done:

## Slide 33: “For” Loop Conversion Example
Carnegie Mellon
C Code
Initial test can be optimized away
#define WSIZE 8*sizeof(int)
int pcount_for(unsigned x) {
int i;
int result = 0;
for (i = 0; i < WSIZE; i++) {
unsigned mask = 1 << i;
result += (x & mask) != 0;
}
return result;
}
Goto Version
int pcount_for_gt(unsigned x) {
int i;
int result = 0;
i = 0;
if (!(i < WSIZE))
goto done;
loop:
{
unsigned mask = 1 << i;
result += (x & mask) != 0;
}
i++;
if (i < WSIZE)
goto loop;
done:
return result;
}
Init
!Test
Body
Update
Test

## Slide 34: Summary
Carnegie Mellon
Today
  Complete addressing mode, address computation (leal)
  Arithmetic operations
  Control: Condition codes
  Conditional branches & conditional moves
  Loops
Next Time
  Switch statements
  Stack
  Call / return
  Procedure call discipline

## Slide 35: Machine-Level Programming III: Switch Statements and IA32 Procedures
Carnegie Mellon

## Slide 36: Today
Carnegie Mellon
Switch statements
IA 32 Procedures
  Stack Structure
  Calling Conventions
  Illustrations of Recursion & Pointers

## Slide 37: Switch Statement Example
Carnegie Mellon
Multiple case labels
  Here: 5 & 6
Fall through cases
  Here: 2
Missing cases
  Here: 4
long switch_eg
(long x, long y, long z)
{
long w = 1;
switch(x) {
case 1:
w = y*z;
break;
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
case 5:
case 6:
w -= z;
break;
default:
w = 2;
}
return w;
}

## Slide 38: Jump Table Structure
Carnegie Mellon
Code Block
0
Targ0:
Code Block
1
Targ1:
Code Block
2
Targ2:
Code Block
n–1
Targn-1:
•
•
•
Targ0
Targ1
Targ2
Targn-1
•
•
•
jtab:
target = JTab[x];
goto *target;
switch(x) {
case val_0:
Block 0
case val_1:
Block 1
• • •
case val_n-1:
Block n–1
}
Switch Form
Approximate Translation
Jump Table
Jump Targets

## Slide 39: Switch Statement Example (IA32)
Carnegie Mellon
long switch_eg(long x, long y, long z)
{
long w = 1;
switch(x) {
. . .
}
return w;
}
Indirect jump
Jump table
.section .rodata
.align 4
.L7:
.long .L2 # x = 0
.long .L3 # x = 1
.long .L4 # x = 2
.long .L5 # x = 3
.long .L2 # x = 4
.long .L6 # x = 5
.long .L6 # x = 6
Setup:
switch_eg:
pushl %ebp # Setup
movl %esp, %ebp # Setup
movl 8(%ebp), %eax # eax = x
cmpl $6, %eax # Compare x:6
ja .L2 # If unsigned > goto default
jmp *.L7(,%eax,4) # Goto *JTab[x]

## Slide 40: Assembly Setup Explanation
Carnegie Mellon
Table Structure
  Each target requires 4 bytes
  Base address at .L7
Jumping
  Direct: jmp .L2
  Jump target is denoted by label .L2
  Indirect: jmp *.L7(,%eax,4)
  Start of jump table: .L7
  Must scale by factor of 4 (labels have 32-bits = 4 Bytes on IA32)
  Fetch target from effective Address .L7 + eax*4
    Only for 0 ≤ x ≤ 6
Jump table
.section .rodata
.align 4
.L7:
.long .L2 # x = 0
.long .L3 # x = 1
.long .L4 # x = 2
.long .L5 # x = 3
.long .L2 # x = 4
.long .L6 # x = 5
.long .L6 # x = 6

## Slide 41: x86-64 Switch Implementation
Carnegie Mellon
.section .rodata
.align 8
.L7:
.quad .L2 # x = 0
.quad .L3 # x = 1
.quad .L4 # x = 2
.quad .L5 # x = 3
.quad .L2 # x = 4
.quad .L6 # X = 5
.quad .L6 # x = 6
Jump Table
Same general idea, adapted to 64-bit code
Table entries 64 bits (pointers)
Cases use revised code
.L3:
movq %rdx, %rax
imulq %rsi, %rax
ret
switch(x) {
case 1: // .L3
w = y*z;
break;
. . .
}

## Slide 42: IA32 Object Code
Carnegie Mellon
Setup
  Label .L2 becomes address 0x8048422
  Label .L7 becomes address 0x8048660
08048410 <switch_eg>:
. . .
8048419: 77 07 ja 8048422 <switch_eg+0x12>
804841b: ff 24 85 60 86 04 08 jmp *0x8048660(,%eax,4)
switch_eg:
. . .
ja .L2 # If unsigned > goto default
jmp *.L7(,%eax,4) # Goto *JTab[x]
Assembly Code
Disassembled Object Code

## Slide 43: Summarizing
Carnegie Mellon
C Control
  if-then-else
  do-while
  while, for
  switch
Assembler Control
  Conditional jump
  Conditional move
  Indirect jump
  Compiler generates code sequence to implement more complex control
Standard Techniques
  Loops converted to do-while form
  Large switch statements use jump tables
  Sparse switch statements may use decision trees

## Slide 44: Today
Carnegie Mellon
Switch statements
IA 32 Procedures
  Stack Structure
  Calling Conventions
  Illustrations of Recursion & Pointers

## Slide 45: IA32 Stack
Carnegie Mellon
Region of memory managed with stack discipline
Grows toward lower addresses
Register %esp contains lowest stack address
  address of “top” element
Stack Pointer: %esp
Stack Grows
Down
Increasing
Addresses
Stack “Top”
Stack “Bottom”

## Slide 46: IA32 Stack
Carnegie Mellon
Stack Pointer: %esp
Stack Grows
Down
Increasing
Addresses
Stack “Top”
Stack “Bottom”
When the stack is upside down, the data do not fall down.
Surprised!

## Slide 47: IA32 Stack: Push
Carnegie Mellon
pushl Src
  Fetch operand at Src
  Decrement %esp by 4
  Write operand at address given by %esp
-4
Stack Grows
Down
Increasing
Addresses
Stack “Bottom”
Stack Pointer: %esp
Stack “Top”

## Slide 48: IA32 Stack: Pop
Stack Pointer: %esp
Stack Grows
Down
Increasing
Addresses
Stack “Top”
Stack “Bottom”
Carnegie Mellon
+4
popl Dest
  Read operand at address %esp
  Increment %esp by 4
  Write operand to Dest

## Slide 49: Procedure Control Flow
Carnegie Mellon
Use stack to support procedure call and return
Procedure call: call label
  Push return address on stack
  Jump to label
Return address:
  Address of the next instruction right after call
  Example from disassembly
  804854e: e8 3d 06 00 00 call 8048b90 <main>
  8048553: 50 pushl %eax
  Return address = 0x8048553
Procedure return: ret
  Pop address from stack
  Jump to address

## Slide 50: Procedure Call Example
0x8048553
0x104
Carnegie Mellon
%esp
%eip
%esp
%eip
0x8048b90
0x108
0x10c
0x110
0x104
0x804854e
123
0x108
0x10c
0x110
123
0x108
call 8048b90
804854e: e8 3d 06 00 00 call 8048b90 <main>
8048553: 50 pushl %eax
%eip: program counter

## Slide 51: Procedure Return Example
Carnegie Mellon
%esp
%eip
0x104
%esp
%eip
0x8048591
0x104
0x108
0x10c
0x110
0x8048553
123
0x108
0x10c
0x110
123
ret
8048591: c3 ret
0x108
0x8048553
0x8048553
%eip: program counter

## Slide 52: Stack-Based Languages
Carnegie Mellon
Languages that support recursion
  e.g., C, Pascal, Java
  Code must be “Reentrant”
    Multiple simultaneous instantiations of single procedure
  Need some place to store state of each instantiation
    Arguments
    Local variables
    Return pointer
Stack discipline
  State for given procedure needed for limited time
    From when called to when return
  Callee returns before caller does
Stack allocated in Frames
  state for single procedure instantiation

## Slide 53: Stack Frames
Carnegie Mellon
Frame Pointer: %ebp
Contents
  Local variables
  Return information
  Temporary space
Management
  Space allocated when enter procedure
    “Set-up” code
  Deallocated when return
    “Finish” code
Stack Pointer: %esp
Stack “Top”
Previous Frame
Frame for proc
They do not fall down!

## Slide 54: IA32/Linux Stack Frame
Carnegie Mellon
Current Stack Frame (“Top” to Bottom)
  “Argument build:” Parameters for function about to call
  Local variables If can’t keep in registers
  Saved register context
  Old frame pointer
Caller Stack Frame
  Return address
    Pushed by call instruction
  Arguments for this call
Return Addr
Saved
Registers
+
Local
Variables
Argument
Build
Old %ebp
Arguments
Caller
Frame
Frame pointer %ebp
Stack pointer
%esp

## Slide 55: Today
Carnegie Mellon
Switch statements
IA 32 Procedures
  Stack Structure
  Calling Conventions
  Illustrations of Recursion & Pointers

## Slide 56: IA32/Linux+Windows Register Usage
Carnegie Mellon
%eax, %edx, %ecx
  Caller saves prior to call if values are used later
%eax
  also used to return integer value
%ebx, %esi, %edi
  Callee saves if wants to use them
%esp, %ebp
  special form of callee save
  Restored to original values upon exit from procedure
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
Caller-Save
Temporaries
Callee-Save
Temporaries
Special

## Slide 57: Today
Carnegie Mellon
Switch statements
IA 32 Procedures
  Stack Structure
  Calling Conventions
  Illustrations of Recursion & Pointers

## Slide 58: Recursive Function
Carnegie Mellon
/* Recursive popcount */
int pcount_r(unsigned x) {
if (x == 0)
return 0;
else return
(x & 1) + pcount_r(x >> 1);
}
Registers
  %eax, %edx used without first saving
  %ebx used, but saved at beginning & restored at end
pcount_r:
pushl %ebp
movl %esp, %ebp
pushl %ebx
subl $4, %esp
movl 8(%ebp), %ebx
movl $0, %eax
testl %eax, %ebx
je .L3
movl %ebx, %eax
shrl %eax
movl %eax, (%esp)
call pcount_r
movl %ebx, %edx
andl $1, %edx
leal (%edx,%eax), %eax
.L3:
addl $4, %esp
popl %ebx
popl %ebp
ret

## Slide 59: Recursive Call #1
Carnegie Mellon
/* Recursive popcount */
int pcount_r(unsigned x) {
if (x == 0)
return 0;
else return
(x & 1) + pcount_r(x >> 1);
}
Actions
  Save old value of %ebx on stack
  Allocate space for argument to recursive call
  Store x in %ebx
pcount_r:
pushl %ebp
movl %esp, %ebp
pushl %ebx
subl $4, %esp
movl 8(%ebp), %ebx
• • •
x
Rtn adr
Old %ebp
%ebp
•
•
•
%esp
Old %ebx
x
%ebx

## Slide 60: Observations About Recursion
Carnegie Mellon
Handled Without Special Consideration
  Stack frames mean that each function call has private storage
    Saved registers & local variables
    Saved return pointer
  Register saving conventions prevent one function call from corrupting another’s data
  Stack discipline follows call / return pattern
    If P calls Q, then Q returns before P
    Last-In, First-Out
Also works for mutual recursion
  P calls Q; Q calls P

## Slide 61: Pointer Code
Carnegie Mellon
/* Compute x + 3 */
int add3(int x) {
int localx = x;
incrk(&localx, 3);
return localx;
}
Generating Pointer
add3 creates pointer and passes it to incrk
/* Increment value by k */
void incrk(int *ip, int k) {
*ip += k;
}
Referencing Pointer

## Slide 62: Creating and Initializing Local Variable
Carnegie Mellon
%esp
int add3(int x) {
int localx = x;
incrk(&localx, 3);
return localx;
}
Variable localx must be stored on stack
  Because: Need to create pointer to it
Compute pointer as -4(%ebp)
First part of add3
x
Rtn adr
Old %ebp
%ebp
0
4
8
-4
localx=x
Unused
-12
-8
-16
add3:
pushl %ebp
movl %esp, %ebp
subl $24, %esp # Alloc. 24 bytes
movl 8(%ebp), %eax
movl %eax, -4(%ebp) # Set localx to x
-20
-24

## Slide 63: Creating Pointer as Argument
Carnegie Mellon
%esp
int add3(int x) {
int localx = x;
incrk(&localx, 3);
return localx;
}
Use leal instruction to compute address of localx
Middle part of add3
x
Rtn adr
Old %ebp
%ebp
0
4
8
-4
localx
Unused
-12
-8
-16
movl $3, 4(%esp) # 2nd arg = 3
leal -4(%ebp), %eax # &localx
movl %eax, (%esp) # 1st arg = &localx
call incrk
-20
-24
3
%esp+4

## Slide 64: Retrieving local variable
Carnegie Mellon
%esp
int add3(int x) {
int localx = x;
incrk(&localx, 3);
return localx;
}
Retrieve localx from stack as return value
Final part of add3
x
Rtn adr
Old %ebp
%ebp
0
4
8
-4
localx
Unused
-12
-8
-16
movl -4(%ebp), %eax # Return val= localx
leave
ret
-20
-24

## Slide 65: IA 32 Procedure Summary
Carnegie Mellon
Important Points
  Stack is the right data structure for procedure call / return
    If P calls Q, then Q returns before P
Recursion (& mutual recursion) handled by normal calling conventions
  Can safely store values in local stack frame and in callee-saved registers
  Put function arguments at top of stack
  Result return in %eax
Pointers are addresses of values
  On stack or global
Return Addr
Saved
Registers
+
Local
Variables
Argument
Build
Old %ebp
Arguments
Caller
Frame
%ebp
%esp