## Slide 1: Machine-Level Programming IV: Data

## Slide 2: Today
Arrays
  One-dimensional
  Multi-dimensional (nested)
  Multi-level
Structures
  Allocation
  Access

## Slide 3: Today
Procedures (x86-64)
Arrays
  One-dimensional
  Multi-dimensional (nested)
  Multi-level
Structures

## Slide 4: Basic Data Types
Integral
  Stored & operated on in general (integer) registers
  Signed vs. unsigned depends on instructions used
    Intel ASM Bytes C
    byte b 1 [unsigned] char
    word w 2 [unsigned] short
    double word l 4 [unsigned] int
    quad word q 8 [unsigned] long int (x86-64)
Floating Point
  Stored & operated on in floating point registers
    Intel ASM Bytes C
    Single s 4 float
    Double l 8 double
    Extended t 10/12/16 long double

## Slide 5: Array Allocation
Basic Principle
  T A[L];
  Array of data type T and length L
  Contiguously allocated region of L * sizeof(T) bytes
char string[12];
x
x + 12
int val[5];
x
x + 4
x + 8
x + 12
x + 16
x + 20
double a[3];
x + 24
x
x + 8
x + 16
char *p[3];
x
x + 8
x + 16
x + 24
x
x + 4
x + 8
x + 12
IA32
x86-64

## Slide 6: Array Access
Basic Principle
  T A[L];
  Array of data type T and length L
  Identifier A can be used as a pointer to array element 0: Type T*
Reference Type Value
  val[4] int 3
  val int * x
  val+1 int * x + 4
  &val[2] int * x + 8
  val[5] int ??
  *(val+1) int 5
  val + i int * x + 4 i
int val[5];
1
5
2
1
3
x
x + 4
x + 8
x + 12
x + 16
x + 20

## Slide 7: Array Example
Declaration “zip_dig cmu” equivalent to “int cmu[5]”
Example arrays were allocated in successive 20 byte blocks
  Not guaranteed to happen in general
#define ZLEN 5
typedef int zip_dig[ZLEN];
zip_dig cmu = { 1, 5, 2, 1, 3 };
zip_dig mit = { 0, 2, 1, 3, 9 };
zip_dig ucb = { 9, 4, 7, 2, 0 };
zip_dig cmu;
1
5
2
1
3
16
20
24
28
32
36
zip_dig mit;
0
2
1
3
9
36
40
44
48
52
56
zip_dig ucb;
9
4
7
2
0
56
60
64
68
72
76

## Slide 8: Array Accessing Example
Register %edx contains starting address of array
Register %eax contains array index
Desired digit at 4*%eax + %edx
Use memory reference (%edx,%eax,4)
int get_digit
(zip_dig z, int dig)
{
return z[dig];
}
# %edx = z
# %eax = dig
movl (%edx,%eax,4),%eax # z[dig]
IA32
zip_dig cmu;
1
5
2
1
3
16
20
24
28
32
36

## Slide 9: Multidimensional (Nested) Arrays
Declaration
  T A[R][C];
  2D array of data type T
  R rows, C columns
  Type T element requires K bytes
Array Size
  R * C * K bytes
Arrangement
  Row-Major Ordering
A[0][0]
A[0][C-1]
A[R-1][0]
• • •
• • •
A[R-1][C-1]
•
•
•
•
•
•
int A[R][C];
• • •
A
[0]
[0]
A
[0]
[C-1]
• • •
A
[1]
[0]
A
[1]
[C-1]
• • •
A
[R-1]
[0]
A
[R-1]
[C-1]
• • •
4*R*C Bytes

## Slide 10: Today
Structures
  Allocation
  Access

## Slide 11: Structure Allocation
struct rec {
int a[3];
int i;
struct rec *n;
};
Concept
  Contiguously-allocated region of memory
  Refer to members within structure by names
  Members may be of different types
Memory Layout
i
a
n
0
12
16
20

## Slide 12: Structure Access
struct rec {
int a[3];
int i;
struct rec *n;
};
IA32 Assembly
# %edx = val
# %eax = r
movl %edx, 12(%eax) # Mem[r+12] = val
void
set_i(struct rec *r,
int val)
{
r->i = val;
}
Accessing Structure Member
  Pointer indicates first byte of structure
  Access elements with offsets
i
a
n
0
12
16
20
r+12
r

## Slide 13: Generating Pointer to Structure Member
movl 12(%ebp), %eax # Get idx
sall $2, %eax # idx*4
addl 8(%ebp), %eax # r+idx*4
int *get_ap
(struct rec *r, int idx)
{
return &r->a[idx];
}
Generating Pointer to Array Element
  Offset of each structure member determined at compile time
  Arguments
    Mem[%ebp+8]: r
    Mem[%ebp+12]: idx
r+idx*4
r
i
a
n
0
12
16
20
struct rec {
int a[3];
int i;
struct rec *n;
};

## Slide 14: Following Linked List
.L17: # loop:
movl 12(%edx), %eax # r->i
movl %ecx, (%edx,%eax,4) # r->a[i] = val
movl 16(%edx), %edx # r = r->n
testl %edx, %edx # Test r
jne .L17 # If != 0 goto loop
void set_val
(struct rec *r, int val)
{
while (r) {
int i = r->i;
r->a[i] = val;
r = r->n;
}
}
C Code
struct rec {
int a[3];
int i;
struct rec *n;
};
i
a
n
0
12
16
20
Element i
Register | Value
%edx | r
%ecx | val

## Slide 15: Summary
Arrays
  One-dimensional
  Multi-dimensional (nested)
Structures
  Allocation
  Access

## Slide 16: The Memory Hierarchy

## Slide 17: Today
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy

## Slide 18: Random-Access Memory (RAM)
Key features
  RAM is traditionally packaged as a chip.
  Basic storage unit is normally a cell (one bit per cell).
  Multiple RAM chips form a memory.
Static RAM (SRAM)
  Each cell stores a bit with a four or six-transistor circuit.
  Retains value indefinitely, as long as it is kept powered.
  Relatively insensitive to electrical noise (EMI), radiation, etc.
  Faster and more expensive than DRAM.
Dynamic RAM (DRAM)
  Each cell stores bit with a capacitor. One transistor is used for access
  Value must be refreshed every 10-100 ms.
  More sensitive to disturbances (EMI, radiation,…) than SRAM.
  Slower and cheaper than SRAM.

## Slide 19: SRAM vs DRAM Summary
Trans. Access Needs Needs
per bit time refresh? EDC? Cost Applications
SRAM 4 or 6 1X No Maybe 100x Cache memories
DRAM 1 10X Yes Yes 1X Main memories,
frame buffers

## Slide 20: Conventional DRAM Organization
d x w DRAM:
  dw total bits organized as d supercells of size w bits
cols
rows
0
1
2
3
0
1
2
3
Internal row buffer
16 x 8 DRAM chip
addr
data
supercell
(2,1)
2 bits
/
8 bits
/
Memory
controller
(to/from CPU)

## Slide 21: Reading DRAM Supercell (2,1)
Step 1(a): Row access strobe (RAS) selects row 2.
Step 1(b): Row 2 copied from DRAM array to row buffer.
Cols
Rows
RAS = 2
0
1
2
3
0
1
2
Internal row buffer
16 x 8 DRAM chip
3
addr
data
2
/
8
/
Memory
controller

## Slide 22: Reading DRAM Supercell (2,1)
Step 2(a): Column access strobe (CAS) selects column 1.
Step 2(b): Supercell (2,1) copied from buffer to data lines, and eventually back to the CPU.
Cols
Rows
0
1
2
3
0
1
2
3
Internal row buffer
16 x 8 DRAM chip
CAS = 1
addr
data
2
/
8
/
Memory
controller
supercell
(2,1)
supercell
(2,1)
To CPU

## Slide 23: Memory Modules
: supercell (i,j)
64 MB
memory module
consisting of
eight 8Mx8 DRAMs
addr (row = i, col = j)
Memory
controller
DRAM 7
DRAM 0
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56
64-bit doubleword at main memory address A
bits
0-7
bits
8-15
bits
16-23
bits
24-31
bits
32-39
bits
40-47
bits
48-55
bits
56-63
64-bit doubleword
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56

## Slide 24: Enhanced DRAMs
Basic DRAM cell has not changed since its invention in 1966.
  Commercialized by Intel in 1970.
DRAM cores with better interface logic and faster I/O :
  Synchronous DRAM (SDRAM)
    Uses a conventional clock signal instead of asynchronous control
    Allows reuse of the row addresses (e.g., RAS, CAS, CAS, CAS)
  Double data-rate synchronous DRAM (DDR SDRAM)
    Double edge clocking sends two bits per cycle per pin
    Different types distinguished by size of small prefetch buffer:
      DDR (2 bits), DDR2 (4 bits), DDR4 (8 bits)
    By 2010, standard for most server and desktop systems
    Intel Core i7 supports only DDR3 SDRAM

## Slide 25: Nonvolatile Memories
DRAM and SRAM are volatile memories
  Lose information if powered off.
Nonvolatile memories retain value even if powered off
  Read-only memory (ROM): programmed during production
  Programmable ROM (PROM): can be programmed once
  Eraseable PROM (EPROM): can be bulk erased (UV, X-Ray)
  Electrically eraseable PROM (EEPROM): electronic erase capability
  Flash memory: EEPROMs with partial (sector) erase capability
    Wears out after about 100,000 erasings.
Uses for Nonvolatile Memories
  Firmware programs stored in a ROM (BIOS, controllers for disks, network cards, graphics accelerators, security subsystems,…)
  Solid state disks (replace rotating disks in thumb drives, smart phones, mp3 players, tablets, laptops,…)
  Disk caches

## Slide 26: Traditional Bus Structure Connecting CPU and Memory
A bus is a collection of parallel wires that carry address, data, and control signals.
Buses are typically shared by multiple devices.
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus

## Slide 27: Memory Read Transaction (1)
CPU places address A on the memory bus.
ALU
Register file
Bus interface
A
0
A
x
Main memory
I/O bridge
%eax
Load operation: movl A, %eax

## Slide 28: Memory Read Transaction (2)
Main memory reads A from the memory bus, retrieves word x, and places it on the bus.
ALU
Register file
Bus interface
x
0
A
x
Main memory
%eax
I/O bridge
Load operation: movl A, %eax

## Slide 29: Memory Read Transaction (3)
CPU read word x from the bus and copies it into register %eax.
x
ALU
Register file
Bus interface
x
Main memory
0
A
%eax
I/O bridge
Load operation: movl A, %eax

## Slide 30: Memory Write Transaction (1)
CPU places address A on bus. Main memory reads it and waits for the corresponding data word to arrive.
y
ALU
Register file
Bus interface
A
Main memory
0
A
%eax
I/O bridge
Store operation: movl %eax, A

## Slide 31: Memory Write Transaction (2)
CPU places data word y on the bus.
y
ALU
Register file
Bus interface
y
Main memory
0
A
%eax
I/O bridge
Store operation: movl %eax, A

## Slide 32: Memory Write Transaction (3)
Main memory reads data word y from the bus and stores it at address A.
y
ALU
register file
bus interface
y
main memory
0
A
%eax
I/O bridge
Store operation: movl %eax, A

## Slide 33: What’s Inside A Disk Drive?
Spindle
Arm
Actuator
Platters
Electronics
(including a
processor
and memory!)
SCSI
connector
Image courtesy of Seagate Technology

## Slide 34: Disk Geometry
Disks consist of platters, each with two surfaces.
Each surface consists of concentric rings called tracks.
Each track consists of sectors separated by gaps.
Spindle
Surface
Tracks
Track k
Sectors
Gaps

## Slide 35: Disk Geometry (Muliple-Platter View)
Aligned tracks form a cylinder.
Surface 0
Surface 1
Surface 2
Surface 3
Surface 4
Surface 5
Cylinder k
Spindle
Platter 0
Platter 1
Platter 2

## Slide 36: Disk Capacity
Capacity: maximum number of bits that can be stored.
  Vendors express capacity in units of gigabytes (GB), where 1 GB = 109 Bytes (Lawsuit pending! Claims deceptive advertising).
Capacity is determined by these technology factors:
  Recording density (bits/in): number of bits that can be squeezed into a 1 inch segment of a track.
  Track density (tracks/in): number of tracks that can be squeezed into a 1 inch radial segment.
  Areal density (bits/in2): product of recording and track density.
Modern disks partition tracks into disjoint subsets called recording zones
  Each track in a zone has the same number of sectors, determined by the circumference of innermost track.
  Each zone has a different number of sectors/track

## Slide 37: Computing Disk Capacity
Capacity = (# bytes/sector) x (avg. # sectors/track) x
(# tracks/surface) x (# surfaces/platter) x
(# platters/disk)
Example:
  512 bytes/sector
  300 sectors/track (on average)
  20,000 tracks/surface
  2 surfaces/platter
  5 platters/disk
Capacity = 512 x 300 x 20000 x 2 x 5
= 30,720,000,000
= 30.72 GB

## Slide 38: Disk Operation (Single-Platter View)
The disk surface
spins at a fixed
rotational rate
By moving radially, the arm can position the read/write head over any track.
The read/write head
is attached to the end
of the arm and flies over
the disk surface on
a thin cushion of air.
spindle
spindle
spindle
spindle
spindle

## Slide 39: Disk Operation (Multi-Platter View)
Arm
Read/write heads
move in unison
from cylinder to cylinder
Spindle

## Slide 40: Disk Structure - top view of single platter
Tracks divided into sectors
Surface organized into tracks
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 41: Disk Access
Head in position above a track
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 42: Disk Access
Rotation is counter-clockwise
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 43: Disk Access – Read
About to read blue sector
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 44: Disk Access – Read
After BLUE read
After reading blue sector
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 45: Disk Access – Read
After BLUE read
Red request scheduled next
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 46: Disk Access – Seek
After BLUE read
Seek for RED
Seek to red’s track
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 47: Disk Access – Rotational Latency
After BLUE read
Seek for RED
Rotational latency
Wait for red sector to rotate around
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 48: Disk Access – Read
After BLUE read
Seek for RED
Rotational latency
After RED read
Complete read of red
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 49: Disk Access – Service Time Components
After BLUE read
Seek for RED
Rotational latency
After RED read
Data transfer
Seek
Rotational
latency
Data transfer
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 50: Disk Access Time
Average time to access some target sector approximated by :
  Taccess = Tavg seek + Tavg rotation + Tavg transfer
Seek time (Tavg seek)
  Time to position heads over cylinder containing target sector.
  Typical Tavg seek is 3—9 ms
Rotational latency (Tavg rotation)
  Time waiting for first bit of target sector to pass under r/w head.
  Tavg rotation = 1/2 x 1/RPMs x 60 sec/1 min
  Typical Tavg rotation = 7200 RPMs
Transfer time (Tavg transfer)
  Time to read the bits in the target sector.
  Tavg transfer = 1/RPM x 1/(avg # sectors/track) x 60 secs/1 min.

## Slide 51: Disk Access Time Example
Given:
  Rotational rate = 7,200 RPM
  Average seek time = 9 ms.
  Avg # sectors/track = 400.
Derived:
  Tavg rotation = 1/2 x (60 secs/7200 RPM) x 1000 ms/sec = 4 ms.
  Tavg transfer = 60/7200 RPM x 1/400 secs/track x 1000 ms/sec = 0.02 ms
  Taccess = 9 ms + 4 ms + 0.02 ms
Important points:
  Access time dominated by seek time and rotational latency.
  First bit in a sector is the most expensive, the rest are free.
  SRAM access time is about 4 ns/doubleword, DRAM about 60 ns
    Disk is about 40,000 times slower than SRAM,
    2,500 times slower then DRAM.

## Slide 52: Logical Disk Blocks
Modern disks present a simpler abstract view of the complex sector geometry:
  The set of available sectors is modeled as a sequence of b-sized logical blocks (0, 1, 2, ...)
Mapping between logical blocks and actual (physical) sectors
  Maintained by hardware/firmware device called disk controller.
  Converts requests for logical blocks into (surface,track,sector) triples.
Allows controller to set aside spare cylinders for each zone.
  Accounts for the difference in “formatted capacity” and “maximum capacity”.

## Slide 53: I/O Bus
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Expansion slots for
other devices such
as network adapters.

## Slide 54: Reading a Disk Sector (1)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
mouse
keyboard
Monitor
Disk
I/O bus
Bus interface
CPU initiates a disk read by writing a command, logical block number, and destination memory address to a port (address) associated with disk controller.

## Slide 55: Reading a Disk Sector (2)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Bus interface
Disk controller reads the sector and performs a direct memory access (DMA) transfer into main memory.

## Slide 56: Reading a Disk Sector (3)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Bus interface
When the DMA transfer completes, the disk controller notifies the CPU with an interrupt (i.e., asserts a special “interrupt” pin on the CPU)

## Slide 57: Solid State Disks (SSDs)
Pages: 512KB to 4KB, Blocks: 32 to 128 pages
Data read/written in units of pages.
Page can be written only after its block has been erased
A block wears out after 100,000 repeated writes.
Flash
translation layer
I/O bus
Page 0
Page 1
Page P-1
…
Block 0
…
Page 0
Page 1
Page P-1
…
Block B-1
Flash memory
Solid State Disk (SSD)
Requests to read and
write logical disk blocks

## Slide 58: SSD Performance Characteristics
Why are random writes so slow?
  Erasing a block is slow (around 1 ms)
  Write to a page triggers a copy of all useful pages in the block
    Find an used block (new block) and erase it
    Write the page into the new block
    Copy other pages from old block to the new block
Sequential read tput 250 MB/s Sequential write tput 170 MB/s
Random read tput 140 MB/s Random write tput 14 MB/s
Rand read access 30 us Random write access 300 us

## Slide 59: SSD Tradeoffs vs Rotating Disks
Advantages
  No moving parts  faster, less power, more rugged
Disadvantages
  Have the potential to wear out
    Mitigated by “wear leveling logic” in flash translation layer
    E.g. Intel X25 guarantees 1 petabyte (1015 bytes) of random writes before they wear out
  In 2010, about 100 times more expensive per byte
Applications
  MP3 players, smart phones, laptops
  Beginning to appear in desktops and servers

## Slide 60: Storage Trends
Metric 1980 1985 1990 1995 2000 2005 2010 2010:1980
$/MB 8,000 880 100 30 1 0.1 0.06 130,000
access (ns) 375 200 100 70 60 50 40 9
typical size (MB) 0.064 0.256 4 16 64 2,000 8,000 125,000
DRAM
SRAM
Metric 1980 1985 1990 1995 2000 2005 2010 2010:1980
$/MB 500 100 8 0.30 0.01 0.005 0.0003 1,600,000
access (ms) 87 75 28 10 8 4 3 29
typical size (MB) 1 10 160 1,000 20,000 160,000 1,500,000 1,500,000
Disk
Metric 1980 1985 1990 1995 2000 2005 2010 2010:1980
$/MB 19,200 2,900 320 256 100 75 60 320
access (ns) 300 150 35 15 3 2 1.5 200

## Slide 61: CPU Clock Rates
1980 1990 1995 2000 2003 2005 2010 2010:1980
CPU 8080 386 Pentium P-III P-4 Core 2 Core i7 ---
Clock
rate (MHz) 1 20 150 600 3300 2000 2500 2500
Cycle
time (ns) 1000 50 6 1.6 0.3 0.50 0.4 2500
Cores 1 1 1 1 1 2 4 4
Effective
cycle 1000 50 6 1.6 0.3 0.25 0.1 10,000
time (ns)
Inflection point in computer history
when designers hit the “Power Wall”

## Slide 62: The CPU-Memory Gap
The gap widens between DRAM, disk, and CPU speeds.
Chart: Year
| 1980.0 | 1985.0 | 1990.0 | 1995.0 | 2000.0 | 2003.0 | 2005.0 | 2010.0
Disk seek time | 87000000 | 75000000 | 28000000 | 10000000 | 8000000 | 8000000 | 8000000 | 8000000
Flash SSD access time | 75000
DRAM access time | 375 | 200 | 100 | 70 | 60 | 55 | 50 | 40
SRAM access time | 300 | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5
CPU cycle time | 1000 | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4
Effective CPU cycle time | 0.3 | 0.25 | 0.1
Disk
DRAM
CPU
SSD

## Slide 63: Locality to the Rescue!
The key to bridging this CPU-Memory gap is a fundamental property of computer programs known as locality

## Slide 64: Today
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy

## Slide 65: Locality
Principle of Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 66: Locality Example
Data references
  Reference array elements in succession (stride-1 reference pattern).
  Reference variable sum each iteration.
Instruction references
  Reference instructions in sequence.
  Cycle through loop repeatedly.
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial locality
Temporal locality
Spatial locality
Temporal locality

## Slide 67: Qualitative Estimates of Locality
Claim: Being able to look at code and get a qualitative sense of its locality is a key skill for a professional programmer.
Question: Does this function have good locality with respect to array a?
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}

## Slide 68: Locality Example
Question: Does this function have good locality with respect to array a?
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}

## Slide 69: Memory Hierarchies
Some fundamental and enduring properties of hardware and software:
  Fast storage technologies cost more per byte, have less capacity, and require more power (heat!).
  The gap between CPU and main memory speed is widening.
  Well-written programs tend to exhibit good locality.
These fundamental properties complement each other beautifully.
They suggest an approach for organizing memory and storage systems known as a memory hierarchy.

## Slide 70: Today
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy

## Slide 71: An Example Memory Hierarchy
Registers
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
cheaper
per byte
Remote secondary storage
(tapes, distributed file systems, Web servers)
Local disks hold files retrieved from disks on remote network servers
Main memory holds disk blocks retrieved from local disks
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from L2 cache
CPU registers hold words retrieved from L1 cache
L2 cache holds cache lines retrieved from main memory
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
costlier
per byte

## Slide 72: Caches
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device.
Fundamental idea of a memory hierarchy:
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1.
Why do memory hierarchies work?
  Because of locality, programs tend to access the data at level k more often than they access the data at level k+1.
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.
Big Idea: The memory hierarchy creates a large pool of storage that costs as much as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.

## Slide 73: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10

## Slide 74: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 75: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)

## Slide 76: General Caching Concepts: Types of Cache Misses
Cold (compulsory) miss
  Cold misses occur because the cache is empty.
Conflict miss
  Most caches limit blocks at level k+1 to a small subset (sometimes a singleton) of the block positions at level k.
    E.g. Block i at level k+1 must be placed in block (i mod 4) at level k.
  Conflict misses occur when the level k cache is large enough, but multiple data objects all map to the same level k block.
    E.g. Referencing blocks 0, 8, 0, 8, 0, 8, ... would miss every time.
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache.

## Slide 77: Examples of Caching in the Hierarchy
Hardware
0
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB page
64-bytes block
64-bytes block
4-8 bytes words
What is Cached?
Web proxy server
1,000,000,000
Remote server disks
OS
100
Main memory
Hardware
1
On-Chip L1
Hardware
10
On/Off-Chip L2
AFS/NFS client
10,000,000
Local disk
Hardware + OS
100
Main memory
Compiler
0
CPU core
Managed By
Latency (cycles)
Where is it Cached?
Disk cache
Disk sectors
Disk controller
100,000
Disk firmware

## Slide 78: Summary
The speed gap between CPU, memory and mass storage continues to widen.
Well-written programs exhibit a property called locality.
Memory hierarchies based on caching close the gap by exploiting locality.

## Slide 79: Cache Memories

## Slide 80: Today
Cache memory organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 81: Cache Memories
Cache memories are small, fast SRAM-based memories managed automatically in hardware.
  Hold frequently accessed blocks of main memory
CPU looks first for data in caches (e.g., L1, L2, and L3), then in main memory.
Typical system structure:
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Cache
memories

## Slide 82: General Cache Organization (S, E, B)
E = 2e lines per set
S = 2s sets
set
line
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size:
C = S x E x B data bytes
valid bit

## Slide 83: Cache Read
E = 2e lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset

## Slide 84: What about writes?
Multiple copies of data exist:
  L1, L2, Main Memory, Disk
What to do on a write-hit?
  Write-through (write immediately to memory)
  Write-back (defer write to memory until replacement of line)
    Need a dirty bit (line different from memory or not)
What to do on a write-miss?
  Write-allocate (load into cache, update line in cache)
    Good if more writes to the location follow
  No-write-allocate (writes immediately to memory)
Typical
  Write-through + No-write-allocate
  Write-back + Write-allocate

## Slide 85: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way,
  Access: 11 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 30-40 cycles
Block size: 64 bytes for all caches.

## Slide 86: Cache Performance Metrics
Miss Rate
  Fraction of memory references not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (in percentages):
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.
Hit Time
  Time to deliver a line in the cache to the processor
    includes time to determine whether the line is in the cache
  Typical numbers:
    1-2 clock cycle for L1
    5-20 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    typically 50-200 cycles for main memory (Trend: increasing!)

## Slide 87: Lets think about those numbers
Huge difference between a hit and a miss
  Could be 100x, if just L1 and main memory
Would you believe 99% hits is twice as good as 97%?
  Consider: cache hit time of 1 cycle miss penalty of 100 cycles
  Average access time:
  97% hits: 1 cycle + 0.03 * 100 cycles = 4 cycles
  99% hits: 1 cycle + 0.01 * 100 cycles = 2 cycles
This is why “miss rate” is used instead of “hit rate”

## Slide 88: Writing Cache Friendly Code
Make the common case go fast
  Focus on the inner loops of the core functions
Minimize the misses in the inner loops
  Repeated references to variables are good (temporal locality)
  Stride-1 reference patterns are good (spatial locality)
Key idea: Our qualitative notion of locality is quantified through our understanding of cache memories.

## Slide 89: Concluding Observations
Programmer can optimize for cache performance
  How data structures are organized
  How data are accessed
    Nested loop structure
    Blocking is a general technique
All systems favor “cache friendly code”
  Getting absolute optimum performance is very platform specific
    Cache sizes, line sizes, associativities, etc.
  Can get most of the advantage with generic code
    Keep working set reasonably small (temporal locality)
    Use small strides (spatial locality)