## Slide 1
Chapter 2
Memory Hierarchy Design
Computer Architecture
A Quantitative Approach, Sixth Edition

## Slide 2: Introduction
Programmers want unlimited amounts of memory with low latency
Fast memory technology is more expensive per bit than slower memory
Solution: organize memory system into a hierarchy
  Entire addressable memory space available in largest, slowest memory
  Incrementally smaller and faster memories, each containing a subset of the memory below it, proceed in steps up toward the processor
Temporal and spatial locality insures that nearly all references can be found in smaller memories
  Gives the allusion of a large, fast memory being presented to the processor
Introduction

## Slide 3: Memory Hierarchy
Introduction

## Slide 4: Memory Performance Gap
Introduction

## Slide 5: Memory Hierarchy Design
Memory hierarchy design becomes more crucial with recent multi-core processors:
  Aggregate peak bandwidth grows with # cores:
    Intel Core i7 can generate two references per core per clock
    Four cores and 3.2 GHz clock
      25.6 billion 64-bit data references/second +
      12.8 billion 128-bit instruction references/second
      = 409.6 GB/s!
    DRAM bandwidth is only 8% of this (34.1 GB/s)
    Requires:
      Multi-port, pipelined caches
      Two levels of cache per core
      Shared third-level cache on chip
Introduction

## Slide 6: Performance and Power
High-end microprocessors have >10 MB on-chip cache
  Consumes large amount of area and power budget
Introduction

## Slide 7: Memory Hierarchy Basics
When a word is not found in the cache, a miss occurs:
  Fetch word from lower level in hierarchy, requiring a higher latency reference
  Lower level may be another cache or the main memory
  Also fetch the other words contained within the block
    Takes advantage of spatial locality
  Place block into cache in any location within its set, determined by address
    block address MOD number of sets in cache
Introduction

## Slide 8: Memory Hierarchy Basics
n sets => n-way set associative
  Direct-mapped cache => one block per set
  Fully associative => one set
Writing to cache: two strategies
  Write-through
    Immediately update lower levels of hierarchy
  Write-back
    Only update lower levels of hierarchy when an updated block is replaced
  Both strategies use write buffer to make writes asynchronous
Introduction

## Slide 9: Memory Hierarchy Basics
Miss rate
  Fraction of cache access that result in a miss
Causes of misses
  Compulsory
    First reference to a block
  Capacity
    Blocks discarded and later retrieved
  Conflict
    Program makes repeated references to multiple addresses from different blocks that map to the same location in the cache
Introduction

## Slide 10: Memory Hierarchy Basics
Speculative and multithreaded processors may execute other instructions during a miss
  Reduces performance impact of misses
Introduction

## Slide 11: Memory Hierarchy Basics
Six basic cache optimizations:
  Larger block size
    Reduces compulsory misses
    Increases capacity and conflict misses, increases miss penalty
  Larger total cache capacity to reduce miss rate
    Increases hit time, increases power consumption
  Higher associativity
    Reduces conflict misses
    Increases hit time, increases power consumption
  Higher number of cache levels
    Reduces overall memory access time
  Giving priority to read misses over writes
    Reduces miss penalty
  Avoiding address translation in cache indexing
    Reduces hit time
Introduction

## Slide 12: Memory Technology and Optimizations
Performance metrics
  Latency is concern of cache
  Bandwidth is concern of multiprocessors and I/O
  Access time
    Time between read request and when desired word arrives
  Cycle time
    Minimum time between unrelated requests to memory
SRAM memory has low latency, use for cache
Organize DRAM chips into many banks for high bandwidth, use for main memory
Memory Technology and Optimizations

## Slide 13: Memory Technology
SRAM
  Requires low power to retain bit
  Requires 6 transistors/bit
DRAM
  Must be re-written after being read
  Must also be periodically refeshed
    Every ~ 8 ms (roughly 5% of time)
    Each row can be refreshed simultaneously
  One transistor/bit
  Address lines are multiplexed:
    Upper half of address: row access strobe (RAS)
    Lower half of address: column access strobe (CAS)
Memory Technology and Optimizations

## Slide 14: Internal Organization of DRAM
Memory Technology and Optimizations

## Slide 15: Memory Technology
Amdahl:
  Memory capacity should grow linearly with processor speed
  Unfortunately, memory capacity and speed has not kept pace with processors
Some optimizations:
  Multiple accesses to same row
  Synchronous DRAM
    Added clock to DRAM interface
    Burst mode with critical word first
  Wider interfaces
  Double data rate (DDR)
  Multiple banks on each DRAM device
Memory Technology and Optimizations

## Slide 16: Memory Optimizations
Memory Technology and Optimizations

## Slide 17: Memory Optimizations
Memory Technology and Optimizations

## Slide 18: Memory Optimizations
DDR:
  DDR2
    Lower power (2.5 V -> 1.8 V)
    Higher clock rates (266 MHz, 333 MHz, 400 MHz)
  DDR3
    1.5 V
    800 MHz
  DDR4
    1-1.2 V
    1333 MHz
GDDR5 is graphics memory based on DDR3
Memory Technology and Optimizations

## Slide 19: Memory Optimizations
Reducing power in SDRAMs:
  Lower voltage
  Low power mode (ignores clock, continues to refresh)
Graphics memory:
  Achieve 2-5 X bandwidth per DRAM vs. DDR3
    Wider interfaces (32 vs. 16 bit)
    Higher clock rate
      Possible because they are attached via soldering instead of socketted DIMM modules
Memory Technology and Optimizations

## Slide 20: Memory Power Consumption
Memory Technology and Optimizations

## Slide 21: Stacked/Embedded DRAMs
Stacked DRAMs in same package as processor
  High Bandwidth Memory (HBM)
Memory Technology and Optimizations

## Slide 22: Flash Memory
Type of EEPROM
Types: NAND (denser) and NOR (faster)
NAND Flash:
  Reads are sequential, reads entire page (.5 to 4 KiB)
  25 us for first byte, 40 MiB/s for subsequent bytes
  SDRAM: 40 ns for first byte, 4.8 GB/s for subsequent bytes
  2 KiB transfer: 75 uS vs 500 ns for SDRAM, 150X slower
  300 to 500X faster than magnetic disk
Memory Technology and Optimizations

## Slide 23: NAND Flash Memory
Must be erased (in blocks) before being overwritten
Nonvolatile, can use as little as zero power
Limited number of write cycles (~100,000)
$2/GiB, compared to $20-40/GiB for SDRAM and $0.09 GiB for magnetic disk
Phase-Change/Memrister Memory
  Possibly 10X improvement in write performance and 2X improvement in read performance
Memory Technology and Optimizations

## Slide 24: Memory Dependability
Memory is susceptible to cosmic rays
Soft errors: dynamic errors
  Detected and fixed by error correcting codes (ECC)
Hard errors: permanent errors
  Use spare rows to replace defective rows
Chipkill: a RAID-like error recovery technique
Memory Technology and Optimizations

## Slide 25: Advanced Optimizations
Reduce hit time
  Small and simple first-level caches
  Way prediction
Increase bandwidth
  Pipelined caches, multibanked caches, non-blocking caches
Reduce miss penalty
  Critical word first, merging write buffers
Reduce miss rate
  Compiler optimizations
Reduce miss penalty or miss rate via parallelization
  Hardware or compiler prefetching
Advanced Optimizations

## Slide 26: L1 Size and Associativity
Access time vs. size and associativity
Advanced Optimizations

## Slide 27: L1 Size and Associativity
Energy per read vs. size and associativity
Advanced Optimizations

## Slide 28: Way Prediction
To improve hit time, predict the way to pre-set mux
  Mis-prediction gives longer hit time
  Prediction accuracy
    > 90% for two-way
    > 80% for four-way
    I-cache has better accuracy than D-cache
  First used on MIPS R10000 in mid-90s
  Used on ARM Cortex-A8
Extend to predict block as well
  “Way selection”
  Increases mis-prediction penalty
Advanced Optimizations

## Slide 29: Pipelined Caches
Pipeline cache access to improve bandwidth
  Examples:
    Pentium: 1 cycle
    Pentium Pro – Pentium III: 2 cycles
    Pentium 4 – Core i7: 4 cycles
Increases branch mis-prediction penalty
Makes it easier to increase associativity
Advanced Optimizations

## Slide 30: Multibanked Caches
Organize cache as independent banks to support simultaneous access
  ARM Cortex-A8 supports 1-4 banks for L2
  Intel i7 supports 4 banks for L1 and 8 banks for L2
Interleave banks according to block address
Advanced Optimizations

## Slide 31: Nonblocking Caches
Allow hits before previous misses complete
  “Hit under miss”
  “Hit under multiple miss”
Do not stall during data miss, fetch instructions
Can be used for out-of-order processors (next chapter)
Advanced Optimizations

## Slide 32: Critical Word First, Early Restart
Critical word first
  Request missed word from memory first
  Send it to the processor as soon as it arrives
Early restart
  Request words in normal order
  Send missed work to the processor as soon as it arrives
Effectiveness of these strategies depends on block size and likelihood of another access to the portion of the block that has not yet been fetched
Advanced Optimizations

## Slide 33: Merging Write Buffer
When storing to a block that is already pending in the write buffer, update write buffer
Reduces stalls due to full write buffer
Do not apply to I/O addresses
Advanced Optimizations
No merging write buffering
Merging Write buffering

## Slide 34: Compiler Optimizations
Loop Interchange
  Swap nested loops to access memory in sequential order
Blocking
  Instead of accessing entire rows or columns, subdivide matrices into blocks
  Requires more memory accesses but improves locality of accesses
Advanced Optimizations

## Slide 35: Blocking
for (i = 0; i < N; i = i + 1)
for (j = 0; j < N; j = j + 1)
{
r = 0;
for (k = 0; k < N; k = k + 1)
r = r + y[i][k]*z[k][j];
x[i][j] = r;
};

## Slide 36: Blocking
for (jj = 0; jj < N; jj = jj + B)
for (kk = 0; kk < N; kk = kk + B)
for (i = 0; i < N; i = i + 1)
for (j = jj; j < min(jj + B,N); j = j + 1)
{
r = 0;
for (k = kk; k < min(kk + B,N); k = k + 1)
r = r + y[i][k]*z[k][j];
x[i][j] = x[i][j] + r;
};

## Slide 37: Hardware Prefetching
Fetch two blocks on miss (include next sequential block)
Advanced Optimizations
Pentium 4 Pre-fetching

## Slide 38: 7. Compiler Optimizations
McFarling [1989] reduced caches misses by 75% on 8KB direct mapped cache, 4 byte blocks in software
Instructions
  Reorder procedures in memory so as to reduce conflict misses
  Profiling to look at conflicts(using tools they developed)
Data
  Merging Arrays: improve spatial locality by single array of compound elements vs. 2 arrays
  Loop Interchange: change nesting of loops to access data in order stored in memory
  Loop Fusion: Combine 2 independent loops that have same looping and some variables overlap
  Blocking: Improve temporal locality by accessing “blocks” of data repeatedly vs. going down whole columns or rows

## Slide 39: Merging Arrays Example
/* Before: 2 sequential arrays */
int val[SIZE];
int key[SIZE];
/* After: 1 array of stuctures */
struct merge {
int val;
int key;
};
struct merge merged_array[SIZE];
Reducing conflicts between val & key; improve spatial locality

## Slide 40: Loop Interchange Example
/* Before */
for (k = 0; k < 100; k = k+1)
for (j = 0; j < 100; j = j+1)
for (i = 0; i < 5000; i = i+1)
x[i][j] = 2 * x[i][j];
/* After */
for (k = 0; k < 100; k = k+1)
for (i = 0; i < 5000; i = i+1)
for (j = 0; j < 100; j = j+1)
x[i][j] = 2 * x[i][j];
Sequential accesses instead of striding through memory every 100 words; improved spatial locality

## Slide 41: Loop Fusion Example
/* Before */
for (i = 0; i < N; i = i+1)
for (j = 0; j < N; j = j+1)
a[i][j] = 1/b[i][j] * c[i][j];
for (i = 0; i < N; i = i+1)
for (j = 0; j < N; j = j+1)
d[i][j] = a[i][j] + c[i][j];
/* After */
for (i = 0; i < N; i = i+1)
for (j = 0; j < N; j = j+1)
{ a[i][j] = 1/b[i][j] * c[i][j];
d[i][j] = a[i][j] + c[i][j];}
2 misses per access to a & c vs. one miss per access; improve spatial locality

## Slide 42: Blocking Example
/* Before */
for (i = 0; i < N; i = i+1)
for (j = 0; j < N; j = j+1){
r = 0;
for (k = 0; k < N; k = k+1){
r = r + y[i][k]*z[k][j];
}
x[i][j] = r;
}
Two Inner Loops:
  Read all NxN elements of z[]
  Read N elements of 1 row of y[] repeatedly
  Write N elements of 1 row of x[]
Capacity Misses a function of N & Cache Size:
  2N3 + N2 => (assuming no conflict; otherwise …)
Idea: compute on BxB submatrix that fits

## Slide 43: Blocking Example
/* After */
for (jj = 0; jj < N; jj = jj+B)
for (kk = 0; kk < N; kk = kk+B)
for (i = 0; i < N; i = i+1)
for (j = jj; j < min(jj+B-1,N); j = j+1) {
r = 0;
for (k = kk; k < min(kk+B-1,N); k = k+1) {
r = r + y[i][k]*z[k][j];
}
x[i][j] = x[i][j] + r;
}
B called Blocking Factor
Capacity Misses from 2N3 + N2 to 2N3/B +N2
Conflict Misses Too?

## Slide 44: Compiler Optimizations

## Slide 45: Compiler Prefetching
Insert prefetch instructions before data is needed
Non-faulting: prefetch doesn’t cause exceptions
Register prefetch
  Loads data into register
Cache prefetch
  Loads data into cache
Combine with loop unrolling and software pipelining
Advanced Optimizations

## Slide 46: Use HBM to Extend Hierarchy
128 MiB to 1 GiB
Smaller blocks require substantial tag storage
Larger blocks are potentially inefficient
One approach (L-H):
  Each SDRAM row is a block index
  Each row contains set of tags and 29 data segments
  29-set associative
  Hit requires a CAS
Advanced Optimizations

## Slide 47: Use HBM to Extend Hierarchy
Another approach (Alloy cache):
  Mold tag and data together
  Use direct mapped
Both schemes require two DRAM accesses for misses
  Two solutions:
    Use map to keep track of blocks
    Predict likely misses
Advanced Optimizations

## Slide 48: Use HBM to Extend Hierarchy
Advanced Optimizations

## Slide 49: 1. Reduce Misses via Larger Block Size
-Compulsory
+Conflict & +Capacity
+Miss Penalty

## Slide 50: 2. Higher Associativity
2:1 Cache Rule:
  Miss Rate DM cache size N ~ Miss Rate 2-way cache size N/2
  Holds for < 128KB
8 Way as effective as Fully SA
Execution time is only final measure!
  Will Clock Cycle time increase?
  external cache +10%,
  internal + 2%

## Slide 51: 3. “Victim Cache”
Combine fast hit time of direct mapped while avoiding conflict misses
Add buffer (small fully SA Cache) to place data discarded from cache (Victim)
Jouppi [1990]: 4-entry victim cache removed 20% to 95% of conflicts for a 4 KB direct mapped data cache
Used in Alpha, HP machines
To Next Lower Level In
Hierarchy
DATA
TAGS
One Cache line of Data
Tag and Comparator
One Cache line of Data
Tag and Comparator
One Cache line of Data
Tag and Comparator
One Cache line of Data
Tag and Comparator

## Slide 52: 4. “Pseudo-Associativity”
Hit Time
Pseudo Hit Time
Miss Penalty
Time
Combine fast hit time of Direct Mapped and have the lower conflict misses of 2-way SA cache
Divide cache: on a miss, check other half of cache to see if there, if so have a pseudo-hit (slow hit)
Drawback: CPU pipeline is hard if hit takes 1 or 2 cycles
  Better for caches not tied directly to processor (L2)
  Used in MIPS R1000 L2 cache, similar in UltraSPARC

## Slide 53: 5. Hardware Prefetching
E.g., Instruction Prefetching
  Alpha 21064 fetches 2 blocks on a miss
  Extra block placed in “stream buffer”
  On miss check stream buffer
Works with data blocks too:
  Jouppi [1990] 1 data stream buffer got 25% misses from 4KB cache; 4 streams got 43%
  Palacharla & Kessler [1994] for scientific programs for 8 streams got 50% to 70% of misses from 2 64KB, 4-way set associative caches
Prefetching relies on having extra memory bandwidth that can be used without penalty

## Slide 54: 6. Software Prefetching
Data Prefetch
  Load data into register (HP PA-RISC loads)
  Cache Prefetch: load into cache (MIPS IV, PowerPC, SPARC v. 9)
  Special prefetching instructions cannot cause faults; a form of speculative execution
Issuing Prefetch Instructions takes time
  Is cost of prefetch issues < savings in reduced misses?
  Higher superscalar reduces difficulty of issue bandwidth

## Slide 55: Summary
Advanced Optimizations