## Slide 1
Chapter 4
Data-Level Parallelism in Vector, SIMD, and GPU Architectures
Computer Architecture
A Quantitative Approach, Sixth Edition

## Slide 2: Introduction
SIMD architectures can exploit significant data-level parallelism for:
  Matrix-oriented scientific computing
  Media-oriented image and sound processors
SIMD is more energy efficient than MIMD
  Only needs to fetch one instruction per data operation
  Makes SIMD attractive for personal mobile devices
SIMD allows programmer to continue to think sequentially
Introduction

## Slide 3: SIMD Parallelism
Vector architectures
SIMD extensions
Graphics Processor Units (GPUs)
For x86 processors:
  Expect two additional cores per chip per year
  SIMD width to double every four years
  Potential speedup from SIMD to be twice that from MIMD!
Introduction

## Slide 4: Vector Architectures
Basic idea:
  Read sets of data elements into “vector registers”
  Operate on those registers
  Disperse the results back into memory
Registers are controlled by compiler
  Used to hide memory latency
  Leverage memory bandwidth
Vector Architectures

## Slide 5: VMIPS
Example architecture: RV64V
  Loosely based on Cray-1
  32 64-bit vector registers
    Register file has 16 read ports and 8 write ports
  Vector functional units
    Fully pipelined
    Data and control hazards are detected
  Vector load-store unit
    Fully pipelined
    One word per clock cycle after initial latency
  Scalar registers
    31 general-purpose registers
    32 floating-point registers
Vector Architectures

## Slide 6: RV64V

## Slide 7: VMIPS Instructions
.vv: two vector operands
.vs and .sv: vector and scalar operands
LV/SV: vector load and vector store from address
Example: DAXPY (Y=a*X+Y) D=double precision
  vsetdcfg 4*FP64 # Enable 4 DP FP vregs
  fld f0,a # Load scalar a
  vld v0,x5 # Load vector X
  vmul v1,v0,f0 # Vector-scalar mult
  vld v2,x6 # Load vector Y
  vadd v3,v1,v2 # Vector-vector add
  vst v3,x6 # Store the sum
  vdisable # Disable vector regs
8 instructions, 258 for RV64V (scalar code)
Vector Architectures

## Slide 8: RISC-V code

## Slide 9: Vector Execution Time
Execution time depends on three factors:
  Length of operand vectors
  Structural hazards
  Data dependencies
RV64V functional units consume one element per clock cycle
  Execution time is approximately the vector length
Convoy
  Set of vector instructions that could potentially execute together
Vector Architectures

## Slide 10: Chimes
Sequences with read-after-write dependency hazards placed in same convoy via chaining
Chaining
  Allows a vector operation to start as soon as the individual elements of its vector source operand become available
Chime
  Unit of time to execute one convoy
  m convoys executes in m chimes for vector length n
  For vector length of n, requires m x n clock cycles
Vector Architectures

## Slide 11: Example
vld v0,x5 # Load vector X
vmul v1,v0,f0 # Vector-scalar multiply
vld v2,x6 # Load vector Y
vadd v3,v1,v2 # Vector-vector add
vst v3,x6 # Store the sum
Convoys:
1 vld vmul
2 vld vadd
3 vst
3 chimes, 2 FP ops per result, cycles per FLOP = 1.5
For 32 element vectors, requires 32 x 3 = 96 clock cycles
Vector Architectures

## Slide 12: Challenges
Start up time
  Latency of vector functional unit
  Assume the same as Cray-1
    Floating-point add => 6 clock cycles
    Floating-point multiply => 7 clock cycles
    Floating-point divide => 20 clock cycles
    Vector load => 12 clock cycles
Improvements:
  > 1 element per clock cycle
  Non-64 wide vectors
  IF statements in vector code
  Memory system optimizations to support vector processors
  Multiple dimensional matrices
  Sparse matrices
  Programming a vector computer
Vector Architectures

## Slide 13: Multiple Lanes
Element n of vector register A is “hardwired” to element n of vector register B
  Allows for multiple hardware lanes
Vector Architectures

## Slide 14: Memory Banks
Memory system must be designed to support high bandwidth for vector loads and stores
Spread accesses across multiple banks
  Control bank addresses independently
  Load or store non sequential words (need independent bank addressing)
  Support multiple vector processors sharing the same memory
Example:
  32 processors, each generating 4 loads and 2 stores/cycle
  Processor cycle time is 2.167 ns, SRAM cycle time is 15 ns
  How many memory banks needed?
    32x(4+2)x15/2.167 = ~1330 banks
Vector Architectures

## Slide 15: Graphical Processing Units
Basic idea:
  Heterogeneous execution model
    CPU is the host, GPU is the device
  Develop a C-like programming language for GPU
  Unify all forms of GPU parallelism as CUDA (Compute Unified Device Architecture) thread
  Programming model is “Single Instruction Multiple Thread”
Graphical Processing Units

## Slide 16: Threads and Blocks
A thread is associated with each data element
Threads are organized into blocks
Blocks are organized into a grid
GPU hardware handles thread management, not applications or OS
Graphical Processing Units

## Slide 17: NVIDIA GPU Architecture
Similarities to vector machines:
  Works well with data-level parallel problems
  Scatter-gather transfers
  Mask registers
  Large register files
Differences:
  No scalar processor
  Uses multithreading to hide memory latency
  Has many functional units, as opposed to a few deeply pipelined units like a vector processor
Graphical Processing Units

## Slide 18: Example
Code that works over all elements is the grid
Thread blocks break this down into manageable sizes
  512 threads per block
SIMD instruction executes 32 elements at a time
Thus grid size = 16 blocks
Block is analogous to a strip-mined vector loop with vector length of 32
Block is assigned to a multithreaded SIMD processor by the thread block scheduler
Current-generation GPUs have 7-15 multithreaded SIMD processors
Graphical Processing Units

## Slide 19: Terminology
Each thread is limited to 64 registers
Groups of 32 threads combined into a SIMD thread or “warp”
  Mapped to 16 physical lanes
Up to 32 warps are scheduled on a single SIMD processor
  Each warp has its own PC
  Thread scheduler uses scoreboard to dispatch warps
  By definition, no data dependencies between warps
  Dispatch warps into pipeline, hide memory latency
Thread block scheduler schedules blocks to SIMD processors
Within each SIMD processor:
  32 SIMD lanes
  Wide and shallow compared to vector processors
Graphical Processing Units

## Slide 20: Example
Graphical Processing Units

## Slide 21: GPU Organization
Graphical Processing Units

## Slide 22: NVIDIA GPU Memory Structures
Each SIMD Lane has private section of off-chip DRAM
  “Private memory”
  Contains stack frame, spilling registers, and private variables
Each multithreaded SIMD processor also has local memory
  Shared by SIMD lanes / threads within a block
Memory shared by SIMD processors is GPU Memory
  Host can read and write GPU memory
Graphical Processing Units

## Slide 23: Pascal Architecture Innovations
Each SIMD processor has
  Two or four SIMD thread schedulers, two instruction dispatch units
  16 SIMD lanes (SIMD width=32, chime=2 cycles), 16 load-store units, 4 special function units
  Two threads of SIMD instructions are scheduled every two clock cycles
Fast single-, double-, and half-precision
High Bandwith Memory 2 (HBM2) at 732 GB/s
NVLink between multiple GPUs (20 GB/s in each direction)
Unified virtual memory and paging support
Graphical Processing Units

## Slide 24: Pascal Multithreaded SIMD Proc.
Graphical Processing Units

## Slide 25: Vector Architectures vs GPUs
SIMD processor analogous to vector processor, both have MIMD
Registers
  RV64V register file holds entire vectors
  GPU distributes vectors across the registers of SIMD lanes
  RV64 has 32 vector registers of 32 elements (1024)
  GPU has 256 registers with 32 elements each (8K)
  RV64 has 2 to 8 lanes with vector length of 32, chime is 4 to 16 cycles
  SIMD processor chime is 2 to 4 cycles
  GPU vectorized loop is grid
  All GPU loads are gather instructions and all GPU stores are scatter instructions
Graphical Processing Units

## Slide 26: SIMD Architectures vs GPUs
GPUs have more SIMD lanes
GPUs have hardware support for more threads
Both have 2:1 ratio between double- and single-precision performance
Both have 64-bit addresses, but GPUs have smaller memory
SIMD architectures have no scatter-gather support
Graphical Processing Units

## Slide 27: Loop-Level Parallelism
Focuses on determining whether data accesses in later iterations are dependent on data values produced in earlier iterations
  Loop-carried dependence
Example 1:
for (i=999; i>=0; i=i-1)
x[i] = x[i] + s;
No loop-carried dependence
Detecting and Enhancing Loop-Level Parallelism

## Slide 28: Loop-Level Parallelism
Example 2:
for (i=0; i<100; i=i+1) {
A[i+1] = A[i] + C[i]; /* S1 */
B[i+1] = B[i] + A[i+1]; /* S2 */
}
S1 and S2 use values computed by S1 in previous iteration
S2 uses value computed by S1 in same iteration
Detecting and Enhancing Loop-Level Parallelism

## Slide 29: Loop-Level Parallelism
Example 3:
for (i=0; i<100; i=i+1) {
A[i] = A[i] + B[i]; /* S1 */
B[i+1] = C[i] + D[i]; /* S2 */
}
S1 uses value computed by S2 in previous iteration but dependence is not circular so loop is parallel
Transform to:
A[0] = A[0] + B[0];
for (i=0; i<99; i=i+1) {
B[i+1] = C[i] + D[i];
A[i+1] = A[i+1] + B[i+1];
}
B[100] = C[99] + D[99];
Detecting and Enhancing Loop-Level Parallelism

## Slide 30: Loop-Level Parallelism
Example 4:
for (i=0;i<100;i=i+1) {
A[i] = B[i] + C[i];
D[i] = A[i] * E[i];
}
Example 5:
for (i=1;i<100;i=i+1) {
Y[i] = Y[i-1] + Y[i];
}
Detecting and Enhancing Loop-Level Parallelism